## Slide 1: Network Applications: Email, DNS
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf22/index.shtml
9/22/2022
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Outline
Admin. and recap
Layered architecture
  Internet layering
Application layer overview
Network applications
  Email
  DNS

## Slide 3: Recap: Layering
  Why layering
    reference model
    modularization
  Concepts
    service, interface, and protocol
    physical vs logical communication
  Key design decision
    end-to-end arguments to place functions in layers

## Slide 4: Some Implications of Layered Architecture
A packet as a stack container
Each layer needs multiplexing and demultiplexing to serve layer above
Hn
Hn-1
…
Ln-1
Has a field to indicate which higher layer requires the service
Ln

## Slide 5
The Hourglass Architecture of the Internet
network
infrastructure
end users
IP4
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
Notes: How about move the line to on top of TCP/UDP?

## Slide 6
Link Layer (Ethernet)
Services (to network layer)
  multiplexing/demultiplexing
    - from/to the network layer
  error detection
  multiple access control
    arbitrate access to shared medium
Interface
  send frames to a directly reachable peer
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 7
Link Layer: Protocol Header (Ethernet)
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP4
link
IP6
IP4
link
IP6
access control
error
detection
multiplexing
/demultiplexing

## Slide 8
Network Layer: IP
Services (to transport layer)
  multiplexing/demultiplexing from/to the transport
  fragmentation and reassembling: partition a fragment into smaller packets
    - removed in IPv6
  error detection
  routing: best-effort to send packets from source to destination
  certain QoS/CoS
  does not provide reliability or reservation
Interface:
  send a packet to a (transport-layer) peer at a specified global destination, with certain QoS/CoS
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW

## Slide 9
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW
Network Layer: IPv4 Header
multiplexing
/demultiplexing
fragmentation / reassembling
error
detection
routing
QoS/CoS

## Slide 10
Transport Layer: UDP
A connectionless service
Does not provide: connection setup, reliability, flow control, congestion control, timing, or bandwidth guarantee
  why is there a UDP?
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 11: Transport Services and APIs
Multiple services and APIs proposed in history
  XTI (X/Open Transport Interface), a slight modification of the Transport Layer Interface (TLI) developed by AT&T.
Commonly used transport-layer service model and API: Socket
  sometimes called "Berkeley sockets" acknowledging their heritage from Berkeley Unix
  a socket has a transport-layer local port number
    e.g., email (SMTP) port number 25, web port number 80
  Application can send data into socket, read data out of socket
  an application process binds to a socket (-a all; -u udp; -n number)
    %netstat -aun
Notes: http://www.techrepublic.com/blog/security/list-open-ports-and-listening-services/
lsof –i -n

## Slide 12: Socket Service Model and API
buffers,
states
buffers,
states
transport
protocol

## Slide 13: Multiplexing/Demultiplexing

## Slide 14
Transport Layer: UDP Header
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP
Ethernet
FDDI
Wireless
UDP
TCP
Telnet
Email
FTP
WWW
multiplexing
/demultiplexing
error
detection

## Slide 15
Transport Layer: TCP
Services
  multiplexing/demultiplexing
  reliable transport
    between sending and receiving processes
    setup required between sender and receiver: a connection-oriented service
  flow control: sender won’t overwhelm receiver
  congestion control: throttle sender when network overloaded
  error detection
  does not provide timing, minimum bandwidth guarantees
Interface:
  send a packet to a (app-layer) peer
IP
Ethernet
FDDI
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 16
Transport Layer: TCP Header
IP
Ethernet
Cable/DSL
Wireless
UDP
TCP
Telnet
Email
FTP
WWW
IP
Ethernet
FDDI
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
multiplexing
/demultiplexing
Reliable
transport
flow control
congestion
control
error
detection

## Slide 17: Secure Socket Layer Architecture
HTTP
POP3

## Slide 18: SSL Record-Layer Packet Format
20: change_cipher
21: alert
22: handshake
23: application

## Slide 19: Summary: The Big Picture of the Internet
Hosts and routers:
  ~ 1 bil. hosts
  autonomous systems organized roughly hierarchical
  backbone links at 100 Gbps
Software:
  datagram switching with virtual circuit support at backbone
  layered network architecture
    use end-to-end arguments to determine the services provided by each layer
  the hourglass architecture of the Internet
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
SSL

## Slide 20
Protocol Formats

## Slide 21: Outline
Admin. and recap
Application layer overview

## Slide 22: Application Layer: Goals
Conceptual + implementation aspects of network application protocols
  client server paradigm
  peer to peer paradigm
  network app. programming
Learn about applications by examining common applications
  smtp/pop
  dns
  http (1, 1.1, /2)
  content distribution
  peer-to-peer

## Slide 23: Network Applications vs. Application-layer Protocols
Network application: communicating, distributed processes
  a process is a program that is running within a host
    a user agent is a process serving as an interface to the user
      web: browser
      streaming audio/video: media player
  processes communicate by an application-layer protocol
    e.g., email, Web
Application-layer protocols
  one “piece” of an app
  define messages exchanged by apps and actions taken
  implementing services by using the service provided by the lower layer, i.e., the transport layer
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 24: App. and Trans.: App. Protocols and their Transport Protocols
Application
e-mail
remote terminal access
Web
file transfer
Internet telephony
remote file server
streaming multimedia
Application
layer protocol
smtp [RFC 821]
telnet [RFC 854]
http [RFC 2068]
ftp [RFC 959]
proprietary
(e.g., Vocaltec)
NFS
proprietary
Underlying
transport protocol
TCP/SSL
TCP
TCP/SSL
TCP
typically UDP
TCP or UDP
typically UDP but moving to http
An application needs to choose the transport protocol

## Slide 25: Client-Server Paradigm
Typical network app has two pieces: client and server
application
transport
network
data link
physical
application
transport
network
data link
physical
Client (C):
initiates contact with server (“speaks first”)
typically requests service from server
for Web, client is implemented in browser; for e-mail, in mail reader
Server (S):
provides requested service to client
e.g., Web server sends requested Web page; mail server delivers e-mail
request
reply

## Slide 26: Client-Server Paradigm: Key Questions
application
transport
network
data link
physical
application
transport
network
data link
physical
request
reply
Key questions to ask about a C-S application
- Is the application extensible?
- Is the application scalable?
- How does the application handle server failures (being robust)?
- How does the application handle security?

## Slide 27: Outline
Admin. and recap
Application layer overview
Network applications
  Email

## Slide 28: Electronic Mail
Still active
  80B emails/day
  3.9B active email boxes
A highly recommended reading: a history of Email development
  linked on the Schedule page

## Slide 29: Demo: SMTP
C: auth login
S: 334 VXNlcm5hbWU6
C: eG11Y25ucw==
S: 334 UGFzc3dvcmQ6
C: MzM0ZjU2MDVkZjE1MDRmOQ==
S: 235 OK Authenticated
C: mail from:xmucnns@sina.com
S: 250 ok
C: rcpt to:qiaoxiang@xmu.edu.cn
S: 250 ok
C: data
S: 354 End data with <CR><LF>.<CR><LF>
C: Date:2022-9-22 12:36
C: From:xmucnns@sina.com
C: To:qiaoxiang@xmu.edu.cn
C: Subject:test smtp
C:
C: Hello, Qiao.
C:
C: .
S: 250 ok queue id 11479549283321
C: quit
S: 221 smtp-97-27.smtpsmail.fmail.bx.sinanode.com
S: Connection closed by foreign host.

## Slide 30: Electronic Mail: Components
Three major components:
User agents
Mail servers
Protocols
  Mail transport protocol
    SMTP
  Mail access protocols
    POP3: Post Office Protocol [RFC 1939]
    IMAP: Internet Mail Access Protocol [RFC 1730]
SMTP
SMTP
SMTP
user mailbox
outgoing
message queue
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
POP3 or
IMAP SMTP

## Slide 31: Email Transport Architecture
http://www.maawg.org/sites/maawg/files/news/MAAWG_Email_Authentication_Paper_2008-07.pdf

## Slide 32: SMTP: Mail Transport Protocol Messages (Envelop Messages)
C: auth login
S: 334 VXNlcm5hbWU6
C: eG11Y25ucw==
S: 334 UGFzc3dvcmQ6
C: MzM0ZjU2MDVkZjE1MDRmOQ==
S: 235 OK Authenticated
C: mail from:xmucnns@sina.com
S: 250 ok
C: rcpt to:qiaoxiang@xmu.edu.cn
S: 250 ok
C: data
S: 354 End data with <CR><LF>.<CR><LF>
C: Date:2021-9-22 12:36
C: From:xmucnns@sina.com
C: To:qiaoxiang@xmu.edu.cn
C: Subject:test smtp
C:
C: Hello, Qiao.
C:
C: .
S: 250 ok queue id 11479549283321
C: quit
S: 221 smtp-97-27.smtpsmail.fmail.bx.sinanode.com
S: Connection closed by foreign host.
Email text different from SMTP protocol message
%telnet smtp.sina.com 25

## Slide 33: Mail Message Data
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
Header lines, e.g.,
  To:
  From:
  Subject:
Body
  the “message”, ASCII characters only
blank
line
header
body
Benefit of separating protocol and msg: easier extensibility

## Slide 34: Message Format: Multimedia Extensions
MIME: multimedia mail extension, RFC 2045, 2056
Additional lines in msg header declare MIME content type
From: xmucnns@sina.com
To: qiaoxiang@xmu.edu.cn
Subject: Network map.
MIME-Version: 1.0
Content-Type: image/jpeg Content-Transfer-Encoding: base64
base64 encoded data .....
.........................
......base64 encoded data
multimedia data
type, subtype,
parameter declaration
method used
to encode data
MIME version
encoded data
Benefit of MIME type: self describing data type, adding extensibility.

## Slide 35: Multipart Type: How Attachment Works
From: xmucnns@sina.com
To: qiaoxiang@xmu.edu.cn
Subject: Network map.
MIME-Version: 1.0
Content-Type: multipart/mixed; boundary=98766789
--98766789
Content-Transfer-Encoding: quoted-printable
Content-Type: text/plain
Hi,
Attached is network topology map.
--98766789
Content-Transfer-Encoding: base64
Content-Type: image/jpeg
base64 encoded data .....
.........................
......base64 encoded data
--98766789--

## Slide 36: POP3 Protocol: Mail Retrieval
Authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
Transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
%telnet pop.sina.com 110
S: +OK sina pop3 server ready
C: user xmucnns
S: +OK welcome to sina mail
C: pass 334f5605df1504f9
S: +OK 4 messages (32377 octets)
C: list
S: +OK 4 messages (32377 octets)
S: 1 10410
S: 2 10748
S: 3 7859
S: 4 3360
S: .
C: retr 4
S: +OK 3360 octets
C: dele 2
C: quit
S: +OK
POP3 server signing off
user successfully logged in
Notes: http://www.electrictoolbox.com/article/networking/pop3-commands/

## Slide 37: Exercise
Register an email address at sina.com
Send an email to the registered email address using smtp
Retrieve using pop

## Slide 38: Evaluation of SMTP/POP/IMAP
Key questions to ask about a C-S application
- extensible?
- scalable?
- robust?
- security?
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP
POP3 or
IMAP SMTP

## Slide 39: Email Security: Spam
Spam (Google)
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://www.securelist.com/en/analysis/204792282/Spam_in_January_2013
https://www.trustwave.com/support/labs/spam_statistics.asp
http://en.wikipedia.org/wiki/Bayesian_spam_filtering
http://www.pcworld.com/article/252206/google_explains_gmails_spam_filtering_process.html

## Slide 40: Email Security Issue: Spam
Source: https://www.statista.com/statistics/420400/spam-email-traffic-share-annual/

## Slide 41: Email Security Issue: Spam
Source: https://www.statista.com/statistics/420391/spam-email-traffic-share/

## Slide 42: Discussion: How May One Handle Email Spams?
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
http://www.slideshare.net/kka7/what-you-need-to-know-about-email-authentication

## Slide 43: Detection Methods Used by GMail
Known phishing scams
Message from unconfirmed sender identity
Message you sent to Spam/similarity to suspicious messages
Administrator-set policies
https://support.google.com/mail/answer/1366858?hl=en
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 44: Email Authentication Approaches
Sender Policy Frame (SPF)
DomainKeys Identified Mail (DKIM) Authenticated Results Chain (ARC)
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
https://dmarc.org/presentations/ARC-Overview-2016Q3-v01.pdf

## Slide 45: Sender Policy Framework (SPF RFC7208)
MUA
MTA
Border Outbound MTA m
Border Inbound MTA
MUA
smtp/submission
smtp
smtp
pop/imap
neighbor MTA
validating MTA
Is my neighbor m a permitted sender for the domain?
https://tools.ietf.org/html/rfc7208
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 46: Key Question for SPF?
How does SPF know if its neighbor MTA is a permitted sender of the domain?
Notes: http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
<selector>._domainkey.example.com
  dig txt <selector>._domainkey.<domain> +short

## Slide 47: DomainKeys Identified Mail (DKIM; RFC 5585)
A domain-level digital signature authentication framework for email, using public key crypto
  E.g., mail.sina.com signs that the message is sent by mail.sina server
Basic idea of public key signature
  Owner has both public and private keys
  Owner uses private key to sign a message to generate a signature
  Others with public key can verify signature
  Assumption: difficult to get private key even w/ public key distributed
Notes: mailing lists or account forwarding
https://blog.returnpath.com/how-to-explain-authenticated-received-chain-arc-in-plain-english-2/
https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 48: DomainKeys Identified Mail (DKIM)
MUA
Signing MTA
MTA
VerifyingMTA
MUA
smtp/submission
smtp
smtp
pop/imap
Is the message signed by the private key of the signing domain?
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 49: Example: RSA
1. Choose two large prime numbers p, q.
(e.g., 1024 bits each)
2. Compute n = pq, z = (p-1)(q-1)
3. Choose e (with e < n) that has no common factors
with z. (e, z are “relatively prime”).
4. Choose d such that ed-1 is exactly divisible by z.
(in other words: ed mod z = 1 ).
5. Public key is (n,e). Private key is (n,d).

## Slide 50: RSA: Signing/Verification
0. Given (n,e) and (n,d) as computed above
1. To sign message, m, compute h = hash(m), then sign with private key
s = h mod n
d
(i.e., remainder when h is divided by n)
d
2. To verify signature s, compute
h’ = s mod n
e
(i.e., remainder when s is divided by n)
e
h = (h mod n)
d
mod n
e
Magic
happens!
The magic is a simple application of Euler’s generalization of
Fermat’s little theorem

## Slide 51: Key Question about DKIM?
How does DKIM retrieve the public key of the author domain?
Notes: http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
<selector>._domainkey.example.com
  dig txt <selector>._domainkey.<domain> +short

## Slide 52: Summary: Some Key Remaining Issues about Email
Basic: How to find the email server of a domain?
Scalability/robustness: how to find multiple servers for the email domain?
Security
  SPF: How does SPF know if its neighbor MTA is a permitted sender of the domain?
  DKIM: How does DKIM retrieve the public key of the author domain?

## Slide 53: Scalability/Robustness
Both scalability and robustness require that multiple email servers serve the same email address
client
need an email server’s IP address
mail
server
mail
server
mail
server
sina.com
sina.com
sina.com
130.132.50.7
130.132.50.8
130.132.50.9
mapping

## Slide 54: Mapping Functions Design Alternatives
mapping
name (e.g., sina.com)
1 IP
mapping
multiple IPs
mapping
multiple IPs
name (e.g., sina.com)

## Slide 55: Mapping Functions Design Alternatives
load balancer (routing)
switch
mapping
name (e.g., sina.com)
1 IP
mapping
name (e.g., sina.com)
1 IP
1 IP

## Slide 56: Outline
Admin. and recap
Layered network architecture
Application layer overview
Network applications
  Email
  DNS

## Slide 57: DNS: Domain Name System
Function
  map between (domain name, service) to value, e.g.,
    (xmu.edu.cn, addr) -> 210.34.0.35
    (xmu.edu.cn, email) -> cmsn1.xmu.edu.cn
routers
DNS
Hostname, Service
Address
servers
clients
Notes: Why name: easy to remember, one-level of indirection

## Slide 58: DNS Records
DNS: stores resource records (RR)
Type=NS
  name is domain (e.g. xmu.edu.cn)
  value is the name of the authoritative name server for this domain
RR format: (name, type, value, ttl)
Type=A
  name is hostname
  value is IP address
Type=CNAME
  name is an alias of a “canonical” (real) name
  value is canonical name
Type=MX
  value is hostname of mail server associated with name
Type=SRV
  general extension for services
Type=TXT
  general txt
http://www.iana.org/assignments/dns-parameters/dns-parameters.xhtml
Type=PTR
  a pointer to another name

## Slide 59: Discussion
Can DNS handle multiple values for the same (name, service)?

## Slide 60: Try DNS: Examples
dig <name> <type>
  Try xmu.edu.cn / others and various types
dig <domain> txt to retrieve spf
http://www.zytrax.com/books/dns/ch9/spf.html
Notes: xmu.edu.cn
taobao.edu.cn
harvard.edu
xmu.edu.cn txt
hotmail.com txt

## Slide 61: Observations
MX can return multiple servers
DNS may rotate the servers in answer
Address can also return multiple addresses
SPF is encoded as the txt type