## Slide 1: Network: Global Internet Routing, Policy Routing Analysis
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf22/index.shtml
11/29/2022
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation

## Slide 3: Admin
Lab 4 due on Dec. 8
  Time to say goodbye to procrastination 
  When submitting your code, make sure it at least can compile
Lab 5 to be posted this week
Class project teams and topics finalized
  You have until Jan. 5 to finish your project
    Code, report, slides and pre-recorded presentation (10-15 minutes)
Guest lecture on Dec. 1

## Slide 4: Recap: Routing Computation using Distance Vector/Bellman-Ford Routing
Distributed computation: At node i, computes
One way to understand BFA is to consider it as a dynamic programming alg, propagating from dest to other nodes
i
j
destination

## Slide 5: Recap: Fixing DV/BFA
Property of BFA
  Bad news may propagate slowly due to loops
Techniques
  Reverse poison
    Avoid two-node loops
  DSDV
    Using destination seq to partition into epochs
    A good example of analysis using global invariants
  Diffusive Update Alg (DUAL)
    Utilize backup routes

## Slide 6: Recap: Link State Routing
Basic idea: instead of distributed computing of routes, only distributed state distribution (synchronization)
Link state distribution can still have much complexity, e.g.,
  out of order delivery
  partition and reconnect
  scalability
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 7: Recap: Internet Routing Architecture
Interdomain routing uses a path vector protocol based on AS topology
  improves scalability, privacy, autonomy
Only a small # of routers (gateways) from each AS in the interdomain level
  improves scalability
Autonomous systems have flexibility to choose their own intradomain routing protocols
  allows autonomy

## Slide 8
b
a
AS C
(RIP intra
routing)
c
AS B
(OSPF intra
routing)
AS A
(OSPF intra
routing)
eBGP
iBGP
Gateway routers participate in intradomain to learn internal routes.
Gateway routers of diff. auto. systems exchange routes using eBGP
Gateway routers of same AS share learned external routes using iBGP.
i
e
f
g
h
d
Inter-AS routers form an overlay
Routing with Autonomous Systems

## Slide 9: Routing with Autonomous Systems
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
border (exterior gateway) routers
interior (gateway) routers

## Slide 10: Summary: Internet Routing Architecture
Autonomous systems have flexibility to choose their own intradomain routing protocols
  allows autonomy
Only a small # of routers (gateways) from each AS in the interdomain level
  improves scalability
Interdomain routing using AS topology instead of detailed topology
  improves scalability/privacy

## Slide 11
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard

## Slide 12
BGP Basic Operations
BGP is a Path Vector protocol
  similar to Distance Vector protocol
  a border gateway sends to a neighbor entire path (i.e., a sequence of ASNs) to a destination, e.g.,
    gateway X sends to neighbor N its path to dest. Z:
path (X,Z) = X,Y1,Y2,Y3,…,Z
  if N selects path(X, Z) advertised by X, then: path (N,Z) = N, path (X,Z)
X
N
Z

## Slide 13
BGP Basic Operations
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
while (connection is ALIVE) exchange UPDATE message select best available route
if route changes, export to neigh.
BGP session

## Slide 14: BGP Messages
Four types of messages
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 15
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)

## Slide 16
BGP Policy Routing Framework:
Label Route Information Sources
Forwarding Information Base (FIB)
OSPF
domain
RIP
domain
BGP
OS kernel
RIP process
RIP routing table
Routing Information Base (RIB)
OSPF process
OSPF Routing table
BGP process
BGP routing table
16

## Slide 17: BGP Policy Routing Framework: Decision Components
routing cache
select best path
export path to neighbors
route selection policy: rank paths
export policy: which paths export to which neighbors
Yale
Qwest
AT&T
Internet2
1 3 0
1 0
17

## Slide 18: BGP Example (1)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IAD
AS I
a2->a1: I can reach
hosts in D; path: D
Route selection policy:
- Shortest AS Path policy:
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
No export to F (effect?)
Choose AD using a1
Export policy controls ingress, i.e., who can use I
Notes: Choose

## Slide 19: BGP Example (2)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local_pref for A
- Shortest AS Path
- Prefer eBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using b
Called hot potato (why?)
Notes: Choose

## Slide 20: BGP Example (3)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local pref A
- Shortest AS Path
- Prefer iBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using i2
Called cold potato (why?)
Notes: Choose

## Slide 21: Observing BGP Paths
Using one of the looking glass servers: http://www.bgp4.as/looking-glasses
https://www.gin.ntt.net/looking-glass/

## Slide 22
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis

## Slide 23
Motivation: Policy Routing Stability
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
preferred
less
preferred
The BAD GADGET example:
- 0 is the destination
- the route selection policy of each AS is to prefer its counter clock-wise neighbor
Policy (preferences) aggregation fails: routing instability !
A policy routing system can be considered as a system to aggregate local preferences, but aggregation may not be always successful.

## Slide 24: General Framework of Preference Aggregation
Also called Social Choice
  Given individual preferences, define a framework to aggregate individual preferences:
    A set of choices: a, b, c, …
    A set of voters 1, 2, …
      Each voter has a preference (ranking) of all choices, e.g.,
        voter 1: a > b > c
        voter 2: a > c > b
        voter 3: a > c > b
    A well-specified aggregation rule (protocol) computes an aggregation of ranking, e.g.,
      Society (network): a > b > c
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 25: Example: Aggregation of Global Preference
S
A
B
D
Choices (for S->D route): SAD, SBD, SABD, SBAD
Voters S, A, B, D
Each voter has a preference, e.g.,
  S: SAD > SBD > SABD > SBAD
  …
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 26: Arrow’s Aggregation Framework
Axioms:
  Transitivity
    if a > b & b > c, then a > c
  Unanimity:
    If all participants prefer a over b (a > b) => a > b
  Independence of irrelevant alternatives (IIA)
    Social ranking of a and b depends only on the relative ranking of a and b among all participants
Result:
  Arrow’s Theorem: Any constitution that respects transitivity, unanimity and IIA is a dictatorship.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem