## Slide 1: Network Layer: Distance Vector Routing, Link State Routing Global Internet Routing (Interdomain, BGP)
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf22/index.shtml
11/24/2022
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
        Distance vector protocols (distributed computing)
        Link state protocols (distributed state synchronization)
      Global Internet routing

## Slide 3: Admin
Overview of projects this afternoon
  2-4 persons per team, at most 3 teams per topic
  FIFS signup with corresponding mentors
    If you choose assignment 4 part 2 as your 2-person project, signup with TA
  If not decided by the end of this week (Nov. 27), teams and topics will be assigned randomly
You have until Jan. 5 to finish your project
    Code, report, slides and pre-recorded presentation
Don’t forget you also have assignment 4 and assignment 5 (to be posted)
So please do NOT procrastinate 

## Slide 4
Recap: Routing Context
Often depends on a graph abstraction:
graph nodes are routers
graph edges are physical links
  links have properties: delay, capacity, $ cost, policy
Goal: determine “good” paths
(sequences of routers) thru
networks from source to dest.
Routing
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 5: Recap: Routing Computation using Distance Vector/Bellman-Ford Routing
Distributed computation: At node i, computes
One way to understand BFA is to consider it as a dynamic programming alg, propagating from dest to other nodes
i
j
destination

## Slide 6: Recap: Fixing DV/BFA
Property of BFA
  Bad news may propagate slowly due to loops
Techniques
  Reverse poison
    Avoid two-node loops
  DSDV
    Using destination seq to partition into epochs
    A good example of analysis using global invariants
  Diffusive Update Alg (DUAL)
    Utilize backup routes

## Slide 7
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison
            destination-sequenced DV (DSDV)

## Slide 8: Destination-Sequenced Distance Vector protocol (DSDV)
Basic idea: use sequence numbers to partition computation
  tags each route with a sequence number
  each destination node D periodically advertises monotonically increasing even-numbered sequence numbers
  when a node realizes that the link it uses to reach destination D is broken, it advertises an infinite metric and a sequence number which is one greater than the previous route (i.e., an odd seq. number)
    the route is repaired by a later even-number advertisement from the destination

## Slide 9: DSDV: More Detail
Let’s assume the destination node is D
There are optimizations but we present a simple version:
  each node B maintains (SB, dB), where SB is the sequence number at B for destination D and dB is the best distance using a neighbor from B to D
Both periodical and triggered updates
  periodically: D increases its seq. by 2 and broadcasts with (SD, 0)
  if B is using C as next hop to D and B discovers that C is no longer reachable
    B increases its sequence number SB by 1, sets dB to , and sends (SB, dB) to all neighbors
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.

## Slide 10: Example
1
1
5
1
X
Will this trigger an update?

## Slide 11: Example
1
1
5
1
X
Will this trigger an update?

## Slide 12: DSDV: Update Alg.
Consider simple version, no optimization
Update after receiving a message
  assume B sends to A its current state (SB, dB)
  when A receives (SB, dB)
      if SB > SA, then // always update if a higher seq#
        SA = SB
        if (dB == ) dA = ; else dA= dB + d(A,B)
      else if SA == SB, then
        if dA > dB + d(A,B) // update for the same seq# only if better route dA= dB + d(A,B) and uses B as next hop
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.

## Slide 13: Example
1
1
5
1
Exercise: update process after D increases its seq# to next even number.

## Slide 14: Claim: DSDV will NEVER Form a Loop
Initially no loop (no one has next hop so no loop)
Derive contradiction if a loop forms after a node processes an update,
  e.g., when A receives the update from B, A decides to use B as next hop and forms a loop
A
B
update

## Slide 15: Technique: Global Invariants
Global Invariant is a very effective method in understanding safety of distributed asynchronous protocols
Invariants are defined over the states of the distributed nodes
Consider any node B.
Let’s identify some invariants over the state of node B, i.e., (SB, dB).

## Slide 16: Invariants of a Single Node B
Some invariants about the state of a node B
  [I1] SB is non-decreasing
  [I2] dB is non-increasing for the same sequence number
time

## Slide 17: Invariants of if A Considers B as Next Hop
Some invariants if A considers B as next hop
  [I3] dA is not
  [I4] SB >= SA
    because A is having the seq# which B last sent to A; B’s seq# might be increased after B sent its state
    [I5] if SB == SA
    then dB < dA because dA is based on dB which B sent to A some time ago, dB < dA since all link costs are positive; dB might be decreased after B sent its state
A
B

## Slide 18
Loop Freedom of DSDV
Consider a critical moment
  A starts to consider B as next hop, and we have a loop
According to invariant I4 for each link in the loop (X considers Y as next hop) : SY >= SX
Two cases:
  exists SY > SX
    by transition along the loop SB > SB
  all nodes along the loop have the same sequence number
    apply I5, by transition along the loop dB > dB
A
B
X
Y
update

## Slide 19: Issue of DSDV
1
1
5
1
X

## Slide 20
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison
            destination-sequenced DV (DSDV)
            diffusive update algorithm (DUAL) and EIGRP

## Slide 21: Basic Idea
DSDV guarantees no loop, but at the price of not using any backup path before destination re-announces reachability.
Basic idea: Sufficient condition to guarantee no loop using backup paths (called switching)?

## Slide 22: Key Idea: Feasible Successors
If the reported distance of a neighbor n is lower than the total distance using primary (current shortest), the neighbor n is a feasible successor
n
p
i

## Slide 23: Intuition
Since the reported distance of B is lower than my total distance, B cannot be using me (along a path) to reach the destination
A
feasible successor
primary
B
D
Notes: Before failure:
- dB < dA
- dB >= dC >= dD >= dE >= dA

## Slide 24: Example
Assume A is destination, consider E
 | Reported Dist. | Total Dist.
Neighbor C |  | 
Neighbor D |  | 
3
4
6
5

## Slide 25: Example
5
1
1
1

## Slide 26: Summary: Distance Vector Routing
Basic DV protocol
  take away: use monotonicity as a technique to understand liveness/convergence
    highly recommended reading of Bersekas/Gallager chapter
Fix counting-to-infinity problem
  DSDV
    Idea: uses sequence number to avoid routing loops
      seq# partitions routing updates from different outside events
      within same event, no loop so long each node only decreases its distance
    Analysis: use global invariants to understand/design safety/no routing loops
  EIRGP (DUAL)
    Idea: introduces a sufficient condition for local recovery
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 27: Discussion: Distance Vector Routing
What do you like about distributed, distance vector routing?
What do you not like about distributed, distance vector routing?
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 28: Churns of DV: One Example
N+2
…
…
1
2
3
N-1
N
N+1
N+3
2N
Initially converged.
All links have cost 1
Event: Cost of 1->2 reduces to 0
Message sequences
Node 2 tells 3. Node 3 tells 4…Node N tells N+1. (N-1 messages)
Node N+1 tells N+2, N+2 tells N+3,…,2N. (N-1 messages)
Now node N-1 tells node N+1
Step 2 repeats
Now node N-2 tells node N+1
…
A total of O(N2) messages

## Slide 29
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)

## Slide 30: Link-State Routing
Basic idea: Not distributed computing, only distributed state distribution
Net topology, link costs are distributed to all nodes
    all nodes have same info
    Each node computes its shortest paths from itself to all other nodes
      standard Dijkstra’s algorithm as path compute alg
      Allows multiple same-cost paths
      Multiple cost metrics per link (for type of service routing)
Most commonly used routing protocol (e.g., OSPF/ISIS) by most networks in Internet

## Slide 31: Example: Link State and Directed Graph (OSPFv2)
https://tools.ietf.org/html/rfc1583#page-12
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 32: Example: Link State and Directed Graph (OSPFv2)
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 33
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)
        data structure to be distributed
        state distribution protocol

## Slide 34: Basic Link State Broadcast Protocol
Basic event structure at node n
  on initialization:
    broadcast LSA[e] for each link e connected to n
  on state change to a link e connected to n:
    broadcast LSA[e] = new status
  on receiving an LSA[e]:
    if (does not have LSA[e]) forwards LSA[e] to all links except the incoming link
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
  ordering of events (link up and down)
  network partitioning and then merge
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 35
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
Link State Broadcast
Node S updates link states connected to it.

## Slide 36
Link State Broadcast
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
To avoid forwarding the same link state announcement (LSA) multiple times (forming a loop), each node remembers the received LSAs.
- Second LSA[S] received by E from C is discarded
- Second LSA[S] received by C from E is discarded as well
- Node H receives LSA[S] from two neighbors, and will discard one of them

## Slide 37: Discussion
Issues of the basic link state protocol?
  Recall: goal is to efficiently distribute to each node to a correct, complete link state map

## Slide 38: Link State Broadcast: Issues
Problem: Out of order delivery
  link down and then up
  A node may receive up first and then down
Solution
  Each link update is given a sequence number: (initiator, seq#, link, status)
    the initiator should increase the seq# for each new update
  If the seq# of an update of a link is not higher than the highest seq# a router has seen, drop the update
  Otherwise, forward it to all links except the incoming link (real implementation using packet buffer)
  Problem of solution: seq# corruption
  Solution: age field (e.g., https://tools.ietf.org/html/rfc1583#page-102)

## Slide 39: Link State Broadcast: Issues
Problem: network partition and then reconnect, how to sync across the reconnected components
Solution: updates are sent periodically

## Slide 40: Link State Broadcast: Issues
Problem: Broadcast redundancy
https://hal.inria.fr/inria-00072756/document

## Slide 41: Hierarchical OSPF
“summarize” distances to nets in own area, advertise to other Area Border routers.
run OSPF routing limited to backbone.
  - Link-state advertisements only in area
  each nodes has detailed area topology; - only know direction (shortest path) to nets in other areas.
Two-level hierarchy: local area, backbone.

## Slide 42: Summary: Link State
Basic LS protocol
  take away: instead of computing routing results using distributed computing, distributed computing is for only link state distribution (synchronization)
Link state distribution can still have much complexity, e.g., out of order delivery, partition and reconnect, scalability
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 43: Roadmap: Routing Computation Architecture Spectrum
Datapath
Distributed Bellman Ford
Distributed Link State
Dijkstra
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Distributed Link State
Distributed Link State
Dijkstra
Dijkstra
Notes: RIP: 1988 RFC1058 OSFPv2: RFC2328

## Slide 44
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
        Distance vector protocols (distributed computing)
        Link state protocols (distributed state synchronization)
      Global Internet routing

## Slide 45: Exercise
Does it work to use DV or LS as we discussed for global Internet routing?
Notes: DV: so many loops,
LS/DV: scalability

## Slide 46: Requirements and Solution of Current Global Internet Routing
Scalability: handle network size (#devices) much higher than typical DV or LS can handle
  Solution: Introduce new abstraction to reduce network (graph) size
Autonomy: allow each network to have individual preference of routing (full control of its internal routing; control/preference of routing spanning multiple networks)
  Solution: hierarchical routing and policy routing
Notes: Other than scale, what else?

## Slide 47: New Abstraction: Autonomous Systems (AS)
Abstract each network as an autonomous system (AS), identified by an AS number (ASN)
Conceptually the global routing graph consists of only autonomous systems as nodes
http://www.bgplookingglass.com/list-of-autonomous-system-numbers

## Slide 48
Routing with Autonomous Systems
Internet routing is divided into intra-AS routing and inter-AS routing
  Intra-AS routing (also called intradomain routing)
    A protocol running insides an AS is called an Interior Gateway Protocol (IGP), each AS can choose its own protocol, such as RIP, E/IGRP, OSPF, IS-IS
  Inter-AS routing (also called interdomain routing)
    A protocol runs among autonomous systems is also called an Exterior Gateway Protocol (EGP)
    The de facto EGP protocol is BGP