## Slide 1: A Taxonomy of Communication Networks
  Qiao Xiang
  https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
  09/16/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin. and recap
A brief introduction to the Internet:
  present
Challenges of Internet networks and apps
A taxonomy of communication networks

## Slide 3: Admin.
If you haven't filled out the survey, please go to the class website to do so

## Slide 4: Recap
A protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission or receipt of a message or other events.
Key Internet milestones and their implications:
  ARPANET is sponsored by ARPA 
  The initial IMPs (routers) were made by a small company 
  Many networks 
  Commercialization 
design should survive failures
  internetworking: need a network to connect networks
keep the network simple
  architecture supporting decentralized, autonomous systems

## Slide 5: Outline
Admin. and recaps
A brief introduction to the Internet
  past
  present

## Slide 6: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet
  Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
data center

## Slide 7: Access: Fiber to the x
http://en.wikipedia.org/wiki/Fiber_to_the_x
Notes: the common form of gigabit Ethernet (1Gbit/s) runs over relatively economical category 5e, category 6, or augmented category 6 unshielded twisted-pair copper cabling but only to 300 ft (91 m). However, 1Gbit/s ethernet over fiber can easily reach tens of miles.

## Slide 8: Access: Fiber to the Premises (FTTP)
Deployed by Verizon, AT&T, Google，
One of the largest comm. construction projects
Notes: Average US:
down: 5.8 MBps
Up: 1.2 Mbps
Google fiber:
Cost: $300/customer
http://en.wikipedia.org/wiki/Fiber_to_the_x
http://www.telecompetitor.com/google-ftth-invades-texas-with-austin-the-next-stop-for-google-fiber/
http://www.youtube.com/watch?v=6uZVqPuq81c

## Slide 9: FTTP Architecture
Notes: http://en.wikipedia.org/wiki/Fiber_to_the_x

## Slide 10: FTTP Architecture
Optical Network Terminal (ONT) box outside dwelling or business
Fiber Distribution Terminal (FDT) in poles or pedestals
Fiber Distribution Hub (FDH) at street cabinet
Optical Line Terminal (OLT) at central office

## Slide 11: FTTP Architecture: To Home

## Slide 12: FTTP Architecture: Fiber Distribution Terminal (FDT)

## Slide 13: FTTP Architecture: Central to Fiber Distribution Hub (FDH)
- Backbone fiber ring on
primary arterial streets
(brown)
- Local distribution fiber
plant (red) meets backbone
at cabinet
FDH

## Slide 14: Access: DSL
Compared with FTTP, copper from cabinet (DSLAM) to home
DSLAM

## Slide 15: Access: Wireless
https://x.company/loon/

## Slide 16: Access: Wireless
https://www.cnet.com/home/internet/starlink-satellite-internet-explained/

## Slide 17: Campus Network
tier-1
Internet
CE
Tier-1
F1 (Firewall)
S1
LB1 (Load balancer)
IPS1 (Intrusion prevention)
F2
S2
LB2
IPS2
S3
S4
VLAN 300
VLAN 400
Tier-2
VLAN 100
R1
S5
IPS3
S6
VLAN 200
Tier-3
Logger

## Slide 18: Data Center Networks
http://www.dailymail.co.uk/sciencetech/article-3369491/Google-s-plan-world-Search-engine-build-half-billion-dollar-data-center-US.html

## Slide 19: Data Center Networks
http://www.dailymail.co.uk/sciencetech/article-3369491/Google-s-plan-world-Search-engine-build-half-billion-dollar-data-center-US.html
Notes: http://www.cse.wustl.edu/~jain/cse570-13/ftp/m_03dct.pdf

## Slide 20: Foundation of Data Center Networks
2
n
1
n
1
2

## Slide 21: Foundation of Data Center Networks: Clos Networks
https://en.wikipedia.org/wiki/Clos_network
Q: How big is m so that each new call can be established w/o moving current calls?
Challenge to the class: If you can move existing calls, it is only m >= n.
Notes: Strict-sense nonblocking Clos networks (m ≥ 2n−1): the original 1953 Clos result[edit]
If m ≥ 2n−1, the Clos network is strict-sense nonblocking, meaning that an unused input on an ingress switch can always be connected to an unused output on an egress switch, without having to re-arrange existing calls. This is the result which formed the basis of Clos's classic 1953 paper. Assume that there is a free terminal on the input of an ingress switch, and this has to be connected to a free terminal on a particular egress switch. In the worst case, n−1 other calls are active on the ingress switch in question, and n−1 other calls are active on the egress switch in question. Assume, also in the worst case, that each of these calls passes through a different middle-stage switch. Hence in the worst case, 2n−2 of the middle stage switches are unable to carry the new call. Therefore, to ensure strict-sense nonblocking operation, another middle stage switch is required, making a total of 2n−1.
If m ≥ n, the Clos network is rearrangeably nonblocking, meaning that an unused input on an ingress switch can always be connected to an unused output on an egress switch, but for this to take place, existing calls may have to be rearranged by assigning them to different centre stage switches in the Clos network.[3] To prove this, it is sufficient to consider m = n, with the Clos network fully utilised; that is, r×n calls in progress. The proof shows how any permutation of these r×n input terminals onto r×n output terminals may be broken down into smaller permutations which may each be implemented by the individual crossbar switches in a Clos network with m = n.
The proof uses Hall's marriage theorem[4] which is given this name because it is often explained as follows. Suppose there are r boys and r girls. The theorem states that if every subset of k boys (for each k such that 0 ≤ k ≤ r) between them know k or more girls, then each boy can be paired off with a girl that he knows. It is obvious that this is a necessary condition for pairing to take place; what is surprising is that it is sufficient.
In the context of a Clos network, each boy represents an ingress switch, and each girl represents an egress switch. A boy is said to know a girl if the corresponding ingress and egress switches carry the same call. Each set of k boys must know at least k girls because k ingress switches are carrying k×n calls and these cannot be carried by less than k egress switches. Hence each ingress switch can be paired off with an egress switch that carries the same call, via a one-to-one mapping. These r calls can be carried by one middle-stage switch. If this middle-stage switch is now removed from the Clos network, m is reduced by 1, and we are left with a smaller Clos network. The process then repeats itself until m = 1, and every call is assigned to a middle-stage switch.

## Slide 22: Data Center Networks: Fat-tree Networks
K-ary fat tree: three-layer topology (edge, aggregation and core)
  k pods w/ each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
    each edge switch connects to k/2 servers & k/2 aggr. switches
    each aggr. switch connects to k/2 edge & k/2 core switches
  (k/2)2 core switches: each connects to k pods
http://www.cs.cornell.edu/courses/cs5413/2014fa/lectures/08-fattree.pdf
Q: How large a network can k-ary support using k-port switches?
Notes: K^3/4
http://www.fiber-optic-tutorial.com/100g-switch-price-and-configuration.html
http://web.stanford.edu/class/ee384y/Handouts/clos_networks.pdf
https://en.wikipedia.org/wiki/Clos_network

## Slide 23: Data Center Networks
For example, Google Jupiter at 1 Pbits/sec bisection bw: 100,000 servers at 10G each
http://conferences.sigcomm.org/sigcomm/2015/pdf/papers/p183.pdf
http://googlecloudplatform.blogspot.com/2015/06/A-Look-Inside-Googles-Data-Center-Networks.html
Notes: http://web.stanford.edu/class/ee384y/Handouts/clos_networks.pdf
https://en.wikipedia.org/wiki/Clos_network

## Slide 24: Recall: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access, e.g.,
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet, Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
data center

## Slide 25: Yale Internet Connection
traceroute www.tsinghua.edu.cn
1 college.net.yale.internal (172.28.201.65) 1.440 ms 1.227 ms 1.453 ms
2 10.1.1.13 (10.1.1.13) 1.359 ms 1.153 ms 1.173 ms 3 level3-10g-asr.net.yale.internal (10.1.4.40) 2.786 ms 6.110 ms 2.547 ms 4 cen-10g-yale.net.yale.internal (10.1.3.102) 2.646 ms 3.242 ms 2.576 ms 5 * * * 6 enrt064hhh-9k-te0-3-0-5.net.cen.ct.gov (67.218.83.254) 5.169 ms 3.797 ms 6.891 ms 7 198.71.46.215 (198.71.46.215) 3.615 ms 3.742 ms 3.931 ms 8 et-10-0-0.1180.rtsw.newy32aoa.net.internet2.edu (198.71.46.214) 6.661 ms 6.532 ms 6.310 ms 9 et-4-0-0.4079.sdn-sw.phil.net.internet2.edu (162.252.70.103) 8.658 ms 8.714 ms 8.666 ms 10 et-1-1-0.4079.rtsw.wash.net.internet2.edu (162.252.70.119) 11.787 ms 30.111 ms 11.900 ms 11 et-8-1-0.4079.sdn-sw.ashb.net.internet2.edu (162.252.70.62) 12.428 ms 16.654 ms 15.862 ms 12 et-7-1-0.4079.rtsw.chic.net.internet2.edu (162.252.70.61) 28.898 ms 28.999 ms 28.908 ms 13 et-3-1-0.4070.rtsw.kans.net.internet2.edu (198.71.47.207) 40.084 ms 39.958 ms 39.695 ms 14 et-8-0-0.4079.sdn-sw.denv.net.internet2.edu (162.252.70.10) 50.195 ms 50.562 ms 50.258 ms 15 et-4-1-0.4079.rtsw.salt.net.internet2.edu (162.252.70.9) 59.707 ms 60.261 ms 59.762 ms 16 et-7-0-0.4079.sdn-sw.lasv.net.internet2.edu (162.252.70.30) 67.555 ms 67.539 ms 67.312 ms 17 et-4-1-0.4079.rtsw.losa.net.internet2.edu (162.252.70.29) 72.419 ms 72.428 ms 72.376 ms ...

## Slide 26: Internet2
\
http://noc.net.internet2.edu/i2network/maps-documentation/maps.html#Internet2 Combined Infrastructure Network Map

## Slide 27: Internet2
http://atlas.grnoc.iu.edu/atlas.cgi?map_name=Internet2%20IP%20Layer

## Slide 28: XMU Internet Connection
Try traceroute from XMU to
www.microsoft.com
www.baidu.com
www.sina.com.cn
www.taobao.com

## Slide 29: Qwest Backbone Map
Qwest (CentryLink) Network Maps
http://www.centurylink.com/business/resource-center/network-maps/
http://www.centurylink.com/business/asset/network-map/ip-mpls-network-nm090930.pdf

## Slide 30: Level3 (now part of LUMEN) Network Map
https://www.lumen.com/en-us/resources/network-maps.html

## Slide 31: Internet ISP Connectivity
Roughly hierarchical
  Divided into tiers
  Tier-1 ISPs are also called backbone providers, e.g., AT&T, Verizon, Sprint, Level 3, Qwest
An ISP runs (private) Points of Presence (PoP) where its customers and other ISPs connect to it
ISPs also connect at (public) Internet Exchange Point (IXP)
  public peering
http://en.wikipedia.org/wiki/List_of_Internet_exchange_points_by_size

## Slide 32: Outline
Admin. and recaps
A brief introduction to the Internet
  past
  present
    topology
    traffic

## Slide 33: Internet (Consumer) Traffic
Notes: http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white_paper_c11-481360.pdf

## Slide 34: Internet Traffic in Perspective
640K ought to be enough for anybody.

## Slide 35: Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps

## Slide 36: Scale
“Developers who have worked at the small scale might be asking themselves why we need to bother when we could just use some kind of out-of the-box solution. For small-scale applications, this can be a great idea. We save time and money up front and get a working and serviceable application. The problem comes at larger scales—there are no off-the-shelf kits that will allow you to build something like Amazon... There’s a good reason why the largest applications on the Internet are all bespoke creations: no other approach can create massively scalable applications within a reasonable budget.”
http://www.evontech.com/symbian/55.html

## Slide 37: Largest Internet Sites in the World
https://www.visualcapitalist.com/wp-content/uploads/2021/01/Country-With-the-Most-Websites.html
Notes: http://www.comscore.com/Insights/Press_Releases/2013/8/comScore_Media_Metrix_Ranks_Top_50_U.S._Web_Properties_for_July_2013

## Slide 38: Largest Internet Sites in the World
https://www.visualcapitalist.com/the-50-most-visited-websites-in-the-world/

## Slide 39: General Complexity
Complexity in highly organized systems arises primarily from design strategies intended to create robustness to uncertainty in their environments and component parts.
  Scalability is robustness to changes to the size and complexity of a system as a whole.
  Evolvability is robustness of lineages to large changes on various (usually long) time scales.
  Reliability is robustness to component failures.
  Efficiency is robustness to resource scarcity.
  Modularity is robustness to component rearrangements.
David Meyer

## Slide 40
Core: Simple Forwarding to Network Functions
Modern networks contain diverse types of equipment beyond simple routing/forwarding
Source: [Sherry, et. al SIGCOMM’12]
Small: <=1k hosts; Medium: 1k-10k; Large: 10k-100k; Very Large: >= 100k
Enterprise networks

## Slide 41: Centralized vs Decentralized (Price of Anarchy)
Autonomous (“Selfish”) App: Assume each link has a latency function le(x): latency of link e when x amount of traffic goes through e:
s
t
l(x) = 1
l(x) = x
total traffic

## Slide 42: Autonomous (“Selfish”) App
Braess’s paradox
Notes: Every increase of 20 ms in latency leads to 1% drop in click-through rate
E-commerce abandonment zone:
  33% users will abandon a site takes longer than 4 sec [Jupiter]

## Slide 43: Decentralized (“Selfish”) Users
2
0
3
1
2 0
2 3 0
1 2 0
1 0
3 1 0
3 0
4
3
preferred
less
preferred

## Slide 44: Decentralized (“Selfish”) Users
2
0
3
1
2 3 0
2 0
1 2 0
1 0
3 1 0
3 0
4
3
preferred
less
preferred

## Slide 45: Distributed vs Centralized
Distributed computing is hard, e.g.,
  FLP Impossibility Theorem
  Arrow’s Impossibility Theorem
Achieved good design for only few specific tasks (e.g., state distribution, leader election). Hence, a trend in networking is Software Defined Networking, which is a way of moving away from generic distributed computing, by focusing on utilizing the few well-understood primitives, in particular logically centralized state.

## Slide 46: Recall: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access, e.g.,
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet, Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
  ~ 58000 ASes; Avg 5.7 hops; (http://bgp.potaroo.net/as2.0/bgp-active.html)
data center

## Slide 47
Roadmap
So far we have looked at only the topology and physical connectivity of the Internet: a mesh of computers interconnected via various physical media
A basic question: how are data (the bits) transferred through communication networks?

## Slide 48: Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
A taxonomy of communication networks

## Slide 49: Taxonomy of Communication Networks
Broadcast networks
  nodes share a common channel; information transmitted by a node is received by all other nodes in the network
  examples: TV, radio
Switched networks
  information is transmitted to a small sub-set (usually only one) of the nodes
communication networks
broadcast networks
switched networks

## Slide 50
Circuit switching: dedicated circuit per call/session:
  e.g., telephone, cellular voice
Packet switching: data sent thru network in discrete “chunks”
  e.g., Internet, cellular data
A Taxonomy of Switched Networks
communication networks
switched networks
broadcast networks
circuit-switched networks (e.g., telephone)
packet-switched networks (e.g., Internet)

## Slide 51
Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
A taxonomy of communication networks
  circuit switched networks

## Slide 52
Circuit Switching
Each link has a number of “circuits”
  sometime we refer to a “circuit” as a channel or a line
An end-to-end connection reserves one “circuit” at each link
First commercial telephone switchboard was opened in 1878 to serve the 21 telephone customers in New Haven
Notes: http://www.classicrotaryphones.com/new-england-operators2_big.jpg

## Slide 53
Circuit Switching: Resources/Circuits (Frequency, Time and others)
Divide link resource into “circuits”
  frequency division multiplexing (FDM)
  time division multiplexing (TDM)
  others such as code division multiplexing (CDM), color/lambda division

## Slide 54: Circuit Switching: The Process
Three phases
  circuit establishment
  data transfer
  circuit termination

## Slide 55
circuit establishment
DATA
data transmission
circuit termination
Host A
Host B
Node 1
Node 2
propagation delay
from A to Node 1
propagation delay
from B To A
processing delay at Node 1
Timing Diagram of Circuit Switching