## Slide 1: Network: Policy Routing Analysis, DHCP
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
12/09/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation

## Slide 3: Admin
Week 15 lab class:
  Lab assignment 3-4 results to be announced
  A quick review on lecture 16-27

## Slide 4: Recap: Internet Routing Architecture
Interdomain routing uses a path vector protocol based on AS topology
  improves scalability, privacy, autonomy
Only a small # of routers (gateways) from each AS in the interdomain level
  improves scalability
Autonomous systems have flexibility to choose their own intradomain routing protocols
  allows autonomy

## Slide 5
b
a
AS C
(RIP intra
routing)
c
AS B
(OSPF intra
routing)
AS A
(OSPF intra
routing)
eBGP
iBGP
Gateway routers participate in intradomain to learn internal routes.
Gateway routers of diff. auto. systems exchange routes using eBGP
Gateway routers of same AS share learned external routes using iBGP.
i
e
f
g
h
d
Inter-AS routers form an overlay
Recap: Routing with Autonomous Systems

## Slide 6: Example: AWS Direct Connect
http://docs.aws.amazon.com/directconnect/latest/UserGuide/Welcome.html

## Slide 7: Recap: BGP as a Policy Routing Framework
routing cache
select best path
export path to neighbors
route selection policy: rank paths
export policy: which paths export to which neighbors
Yale
Qwest
AT&T
Internet2
1 3 0
1 0

## Slide 8
Recap: Policy Routing as a Preference Aggregation System
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
preferred
less
preferred
The BAD GADGET example:
- 0 is the destination
- the route selection policy of each AS is to prefer its counter clock-wise neighbor
Policy (preferences) aggregation fails: routing instability !
A policy routing system can be considered as a system to aggregate individual preferences, but aggregation may not be always successful.

## Slide 9: Recap: General Framework of Preference Aggregation
Also called Social Choice
  Given individual preferences, define a framework to aggregate individual preferences:
    A set of choices: a, b, c, …
    A set of voters 1, 2, …
      Each voter has a preference (ranking) of all choices, e.g.,
        voter 1: a > b > c
        voter 2: a > c > b
        voter 3: a > c > b
    A well-specified aggregation rule (protocol) computes an aggregation of ranking, e.g.,
      Society (network): a > b > c
For more details: see Semih Salihoglu (2007). Interdomain Routing as a Social Choice.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 10: Example: Aggregation of Global Preference
S
A
B
D
Choices (for S->D route): SAD, SBD, SABD, SBAD
Voters S, A, B, D
Each voter has a preference, e.g.,
  S: SAD > SBD > SABD > SBAD
  …
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 11: Recap: Arrow’s Aggregation Framework
Axioms:
  Transitivity
    if a > b & b > c, then a > c
  Unanimity:
    If all participants prefer a over b (a > b) => a > b
  Independence of irrelevant alternatives (IIA)
    Social ranking of a and b depends only on the relative ranking of a and b among all participants
Result:
  Arrow’s Theorem: Any constitution that respects transitivity, unanimity and IIA is a dictatorship.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 12: Proofs of Arrow’s Theorem
There are quite a few proofs, and the six-page paper linked on the Schedule page gives three simple proofs.
Below, I give the key insight of the proof using approach 1.

## Slide 13: The Extremal Lemma
Let choice b be chosen arbitrarily. Assume that every voter puts b at the very top or the very bottom of his ranking. Then society must as well (even if half voters put b at the top and half at the bottom)
Proof: by contradiction.
  Assume there exist a and c such that society has a >= b; b >= c.
    By transitivity, a >= c
  We can move c above a w/o changing ab or cb votes, leading to c > a
    By unanimity, c > a

## Slide 14: Step 1: Existence of Pivotal Voter
Let choice b be chosen arbitrarily. There exist a voter n* = n(b) who is extremely pivotal for b in the sense that by changing his vote at some profile, he can move b from the very bottom to the very top in the social ranking.
Proof:
  Consider an extreme profile where b is at the bottom of each voter.
  Consider voter from 1 to n, and we move b from bottom to top one-by-one.
  The first voter whose change causes b to move to the top is n*
    By unanimity, this change must happen at the latest when n*=n

## Slide 15: Step 2: n*=n(b) is dictator of any pair ac not involving b
Proof
  Consider a from ac pair. We show that if a >n* c, then constitution protocol has a > c
  Let profile before n* moves b to top as profile I
  Let profile after n* moves b to top as profile II
  Construct profile III from II by letting n* move a above b; all others can arrange ac as they want, but leave b in extreme position
    a>b in profile I, and a,b is equivalent by IIA in profiles I and III
    b>c in profile II, and bc is equivalent by IIA in profiles II and III
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
.
.
.
b
b
.
.
.
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
1 2 n* . N
b
.
.
.
b
.
.
.
a
b
.
c
.
.
.
b
.
.
.
b
Constitution protocol: b bottom
Constitution protocol : b top
Profile I
Profile II
Profile III
Constitution protocol: a > b since ab same as I
b > c since bc same as II

## Slide 16: Step 3: n* is dictator for every pair ab
Consider c not equal to a or b
There exists n(c) who is a dictator of any pair not involving c, such as the pair ab, i.e.,
  For any profile, if a >n(c) > b, a > b in constitution protocol
n(c) must be n*
  Assume not.
    Consider Profile I and Profile II.
    Since n(c) is not n*, n(c) ranking of ab does not change in Profile I and Profile II.
    When n* changes ab ranking between Profile I and Profile II, the global ranking of ab changes.
    Contradiction.

## Slide 17
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation

## Slide 18: BGP w/ Local Preference
BGP preferences are typically local (only on paths start from itself)
Hence the preferences have dependency (priority)
  The “closer” a node to the destination, the more “powerful” it may be
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10
18

## Slide 19: Complete Dependency: P-Graph
Complete dependency can be captured by a structure called P-graph
Nodes in P-graph are feasible paths
Edges represent priority (low to high)
  A directed edge from path N1P1 to P1
    intuition: to let N1 choose N1P1, P1 must be chosen and exported to N1
  A directed edge from a lower ranked path to a higher ranked path
    intuition: the higher ranked path should be considered first
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10
Any observation on the P-graph?
19

## Slide 20: P-Graph and BGP Convergence
If the P-graph of the networks has no loop, then policy routing converges.
  intuition: choose the path node from the partial order graph with no out-going edge to non-fixed path nodes, fix the path node, eliminate all no longer feasible; continue
Example: suppose we swap the order of 30 and 320
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
30
320
210
20
130
10
20

## Slide 21
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation
            Economics and interdomain routing patterns

## Slide 22
Internet Economy: Two Types of Business Relationship
Customer provider relationship
  a provider is an AS that connects the customer to the rest of the Internet
  customer pays the provider for the transit service
  e.g., Yale is a customer of AT&T and QWEST
Peer-to-peer relationship
  mutually agree to exchange traffic between their respective customers only
  there is no payment between peers
provider
customer
peer
peer
provider
provider to
customer
22

## Slide 23: Route Selection Policies and Economics
Route selection (ranking) policy:
  the typical route selection policy is to prefer customers over peers/providers to reach a destination, i.e., Customer > pEer/Provider
provider
customer
peer
23

## Slide 24
customer
provider
customer
peer
Export Policies and Economics
provider
provider
customer
peer
peer
provider
customer
peer
Routes learned from a customer are sent to all other neighbors
Routes learned from a provider are sent only to customers
Routes learned from a peer are sent only to customers
case 1: routes learned from customer
case 2: routes learned from provider
case 3: routes learned from peer
24

## Slide 25
Example: Typical Export -> No-Valley Routing
P1
A
P2
IP traffic
A advertises path to C, but not P2
A advertises to C paths to P1 and P2
A advertises path to C, but not P1
Suppose P1 and P2 are providers of A; A is a provider of C
C
A learns paths to C, P1, P2
25

## Slide 26: Typical Export Policies Route Patterns
Assume a BGP path SABCD to destination AS D. Consider the business relationship between each pair:
Three types of business relationships:
  PC (provider-customer)
  CP (customer-provider)
  PP (peer-peer)
S A B C D

## Slide 27: Typical Export Policies Route Patterns
Invariant 1 of valid BGP routes (with labels representing business relationship)
P C
?
P C
P C
Dest
P C
Reasoning: only route learned from customer is sent to provider; thus
after a PC, it is always PC to the destination
Notes: If PC, then PC all the way to destination
If CP/PP, all preceding is CP

## Slide 28: Typical Export Policies Route Patterns
Invariant 2 of valid BGP routes (with labels representing business relationship)
CP
?
CP
CP
······
Dest
Reasoning: routes learned from peer or provider are sent to only customers; thus all relationship before is CP.
/PP
Notes: If PC, then PC all the way to destination
If CP/PP, all preceding is CP

## Slide 29: Stability of BGP Policy Routing
Suppose
  there is no loop formed by provider-customer relationship in the Internet
  each AS uses typical route selection policy:
    C > E/P
  each AS uses the typical export policies
Then policy routing always converges (i.e., is stable).

## Slide 30: Case 1: A Link is PC
PC
Proof by contradiction. Assume a loop in P-graph. Consider a fixed link. in the loop
PC
PC
AS 1
AS 2
AS 3
AS 4

## Slide 31: Case 2: Link is CP/PP
CP/PP
CP/PP
CP
CP/PP
CP
AS 1
AS 2
AS 3
AS 4

## Slide 32
Summary: BGP Policy Routing
Advantage
  satisfies current demand
Issues
  policy dispute can lead to instability
    current Internet economy provides a stability framework, but if the framework changes, we may see instability
  Hierarchical routing can be inefficient
AS 4
AS 3
AS 2
AS 1

## Slide 33: Routing: Remaining Issue
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
Naïve design is to send individual host D’s IP. Can we do better?
a1
a2
d
a1->i: I can reach
hosts in D; my path: AD
E
F
AS I
d1
d2
Notes: How to specify hosts in D

## Slide 34
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation
            Economics and interdomain routing patterns
          IP addresses for Interdomain routing

## Slide 35: IP Addressing Scheme: Requirements
Uniqueness: We need an address to uniquely identify each destination
Aggregability : Routing scalability needs flexibility in aggregation of destination addresses
  we want to aggregate as a large set of destinations as possible in BGP announcements
Current: the unit of routing in the Internet is a classless interdomain routing (CIDR) address

## Slide 36
IP Address: Uniqueness
IPv4 address: A 32-bit unique identifier for an interface
interface:
  routers typically have multiple interfaces
  host may have multiple interfaces
  %/sbin/ifconfig -a
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.3.2 = 11011111 00000001 00000011 00000010
223
1
2
3
e.g., /etc/sysconfig/network-scripts/ifcfg-enp0s25
%ifup

## Slide 37: IP Addressing: Class-ful Addressing
given notion of “network”, let’s re-examine IP addresses:
“class-ful” addressing in the original IP design:
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
240.0.0.0 to
255.255.255.255

## Slide 38: Classless InterDomain Routing (CIDR) Address: Aggregation
A CIDR address partitions an IP address into two parts
  A prefix representing the network portion, and the rest (host part)
  address format: a.b.c.d/x, where x is # bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23
Some systems use mask (1’s to indicate network bits), instead of the /x format

## Slide 39: CIDR Aggregation in BGP
AS A
(OSPF)
AS D
i
a1
a2
d
i->a1: I can reach
130.132.0/22; my path: I
AS I
d1
130.132.0.0/24
130.132.2.0/24
130.132.3.0/24
intradomain routing uses /24
130.132.1.0/24
Notes: Does not have to be 24; some can be, say 22.

## Slide 40: CIDR Aggregation in BGP
x00/24: B
x01/24: C
x10/24: E
x/22: A
x11/24: F
A
B
C
E
F
G
x11/24: F
x11/24: GF
F
Problem at S：
Overlapping routing entries.
Solution：
Longest prefix matching (LPM)
S

## Slide 41: Routing Table Size of BGP (number of globally advertised, aggregated entries)
Active BGP Entries (http://bgp.potaroo.net/as1221/bgp-active.html)
Internet Growth
(http://www.caida.org/research/topology/as_core_network/historical.xml)

## Slide 42: IP Addressing: How to Get One?
Q: How does an ISP get its block of addresses?
A: Local Internet Registry (LIR) or National Internet Registry (NIR)
Use
%whois <IP address>
to check who is allocated the given address.
https://www.iana.org/numbers
https://www.iana.org/assignments/ipv4-address-space/ipv4-address-space.xhtml

## Slide 43: IP addresses: How to Get One?
Q: How does a host get an IP address?
A:
  Static configured
    unix: %/sbin/ifconfig eth0 inet 192.168.0.10 netmask 255.255.255.0
  DHCP: Dynamic Host Configuration Protocol (RFC2131): dynamically get address from a DHCP server

## Slide 44: DHCP Goal and History
Goal: allow host to dynamically obtain its IP address from network server when it joins network
History
  1984 Reverse ARP (RFC903): obtain IP address, but at link layer, and hence requires a server at each network link
  1985 Bootstrap Protocol (BOOTP; RFC951): introduces the concept of a relay agent to forward across networks
  1993 DHCP (RFC1531): based on BOOTP but can dynamically allocate and reclaim IP addresses in a pool, as well as delivery of other parameters
  1993 Errors in editorials led to immediate reissue as RFC1541
  1997 DHCP (RFC2131): add DHCPINFORM

## Slide 45: Exercise
DHCP wireshark example

## Slide 46: DHCP: Dynamic Host Configuration Protocol
The often used DORA model (4 messages)
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 47
https://www.ietf.org/rfc/rfc2131.txt

## Slide 49: Exercise
DHCP lease renew

## Slide 50: Optional Read: IP Multicast

## Slide 51
IP Multicast: Service Model
Multicast group concept: use of indirection
  A group is identified by a location-independent logical address (class D IP address: prefix 1110)
Open group model
  Anyone can send packets to the “logical” group address
  Anyone can join a group and receive packets
Normal, best-effort delivery semantics of IP
128.119.40.186
128.59.16.12
128.34.108.63
128.34.108.60
multicast
group
226.17.30.197
Needed: infrastructure to deliver mcast-addressed datagrams to all hosts that have joined that multicast group

## Slide 52
Multicast Across LANs
shared tree
source-based trees
Goal: find a tree (or trees) connecting routers having local mcast group members
  source-based: different tree from sender to each receiver
      Distance-vector multicast routing protocol (DVMRP)
      Protocol-independent multicast-dense mode (PIM-DM)
  shared-tree: same tree used by all group members
      Core-Based Tree (CBT)
      Protocol-independent multicast-sparse mode (PIM-SM)

## Slide 53: Source Tree: Reverse Path Flooding (RPF)
A router x forwards a packet from source (S) iff it arrives via neighbor y, and y is on the shortest path from x back to S
A packet is replicated to all but the incoming interface
x
y
t
S
a
z
1
1
1
1
1

## Slide 54
Reverse Path Forwarding: Improvement
Basic idea: forward a packet from S only on child links for S
A child link of router x for source S
  a link that has x as parent on the shortest path from the link to S
  a child x notifies its parent y (through the routing protocol) that it has selected y as its parent
x
y
t
S
a
z

## Slide 55
Reverse Path Forwarding: Pruning
No need to forward datagrams down subtree with no mcast group members
“prune” msgs sent upstream by router with no downstream group members
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
prune message
LEGEND
S: source
links with multicast
forwarding
P
P
P

## Slide 56: Pruning
Prune (Source, Group) at a leaf router if no members
  send No-Membership Report (NMR) up tree
If all children of router R prune (S,G)
  propagate prune for (S,G) to its parent
What do you do when a member of a group (re)joins?
  send a Graft message to upstream parent
How to deal with failures?
  prune dropped
  flow is reinstated
  down stream routers re-prune
Note: again a soft-state approach

## Slide 57: Implementation of Source Trees in the Internet
Multicast OSFP (MOSFP)
  Membership is part of the link state distribution; calculate source specific, pre-pruned trees
Reverse Path Forwarding
  Distance Vector Multicast Routing Protocol (DVMRP)
  Protocol Independent Multicast – Dense Mode (PIM-DM)
    very similar to DVMRP
  Difference: PIM uses any unicast routing algorithm to determine the path from a router to the source; DVMRP uses distance vector
  Question: the state requirement of Reverse Path Forwarding

## Slide 58: Building a Shared Tree
Steiner Tree: minimum cost tree connecting all routers with attached group members
A Steiner tree is not a spanning tree because you do not need to connect all nodes in the network
Problem is NP-hard
Excellent heuristics exists
Not used in practice:
  computational complexity
  information about entire network needed
  monolithic: rerun whenever a router needs to join/leave

## Slide 59
Center (Core) based Shared Tree
Single delivery tree shared by all
One router identified as “center” of tree
Tree construction is receiver-based
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
A sender unicasts a packet to center
  The packet is distributed on the tree when it hits the tree

## Slide 60: Example: M3 Joins
Group members: M1, M2
core
M1
M2
M3
shared tree
S1
join message
Discussion: what is property of the constructed tree?

## Slide 61: Example: M1 Sends Data
Group members: M1, M2, M3
M1 sends data
core
M1
M2
M3
control (join) messages
data
S1

## Slide 62: Shared Tree Protocols in the Internet
Core Based Tree
Protocol Independent Multicast (PIM) Sparse mode
The catch: how do you know the center?
  session announcement

## Slide 63
Mbone: Tunneling
Q: How to connect “islands” of multicast routers in a “sea” of unicast routers?
mcast datagram encapsulated inside “normal” (non-multicast-addressed) datagram
normal IP datagram sent thru “tunnel” via regular IP unicast to receiving mcast router
receiving mcast router unencapsulates to get mcast datagram
physical topology
logical topology