## Slide 1: CS433/533: Computer Networks
Y. Richard Yang
http://zoo.cs.yale.edu/classes/cs433/
8/31/2017

## Slide 2: Outline
Administrative trivia’s
What is a network protocol?
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
Summary

## Slide 3: Personnel
Instructor
  Y. Richard Yang, yry@cs.yale.edu, AKW 208A
    office hours
      TTh 4:00-5:00 pm or by appointment
      please feel free to stop by if you see I am in my office
Teaching assistants
  Qiao Xiang, AKW 204
    office hours TBA
  Geng Li, AKW 204
    office hours TBA

## Slide 4: Textbook
Textbook
  Computer Networking: A Top-Down Approach, 7/e by Jim Kurose and Keith Ross
Reference books
  Computer Networks by Tanenbaum and Wetherall
  Computer Networks, A Systems Approach by Larry Peterson and Bruce Davie
  TCP/IP Illustrated, Volume 1: The Protocols by W. Richard Stevens
  Java Network Programming, by Elliotte Harold
Resources
  http://zoo.cs.yale.edu/classes/cs433
on

## Slide 5: What are the Goals of this Course?
Learn design principles and techniques of:
  the Internet infrastructure (Internet service provider, data center, cloud)
  large-scale Internet applications
Focus on how the principles and techniques apply and adapt in real world:
  real examples from the Internet

## Slide 6: CPSC433/533 or EENG 452
CPSC433/533: More from a computer science’s view, emphasizing more on programming
EENG 452: More from an engineering’s view, emphasizing more on analysis

## Slide 7: What Do You Need To Do?
Please return the class background survey
  help us determine your background
  help us determine the depth, topics, and assignments
  suggest topics that you want to be covered (if you think of a topic later, please send me email)
Your workload
  homework assignments
    written assignments
    programming assignments
      one HTTP 1.1 server, one TCP, and one robot network using Raspberry Pi or BeagleBone
      two exams

## Slide 8: Grading
Subject to change after I know more about your background
More important is what you realize/learn than the grades !!
Exams | 30%
Assignments | 60%
Class Participation | 10%

## Slide 9: Questions?

## Slide 10: Outline
Administrative trivia’s
What is a network protocol?

## Slide 11: What is a Network Protocol?
A network protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of a message or other events.

## Slide 12: Example Protocol: Simple Mail Transfer Protocol (SMTP)
Messages from a client to a mail server
  HELO
  MAIL FROM: <address>
  RCPT TO: <address>
  DATA <This is the text end with a line with a single .>
  QUIT
Messages from a mail server to a client
  status code
    The first digit of the response broadly indicates the success, failure, or progress of the previous command.
      1xx - Informative message
      2xx - Command ok
      3xx - Command ok so far, send the rest of it.
      4xx - Command was correct, but couldn't be performed for some reason.
      5xx - Command unimplemented, or incorrect, or a serious program error occurred.
  content
user mailbox
outgoing
message queue
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP
POP3,
IMAP SMTP
Command: %telnet netra.cs.yale.edu smtp
Notes: RCPT TO: <> notify=success,failure

## Slide 13: Example Protocol: TCP Connection Close Protocol
Why connection close?
  so that each side can release resource and remove state about the communication
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?

## Slide 14: General Case: The Two-Army Problem
The gray (blue) armies need to agree on whether or not they will attack the white army. They achieve agreement by sending messengers to the other side. If they both agree, attack; otherwise, no. Note that a messenger can be captured!

## Slide 15: Example: TCP Protocol Handshakes
Host A
Host B
ACK(seq=x), SYN(seq=y)
SYN(seq=x)
ACK(seq=y)
DATA(seq=x+1)
ACK
FIN
ACK
FIN
ACK

## Slide 16: Example: Google’ new QUIC
http://conferences.sigcomm.org/sigcomm/2017/files/program/ts-5-1-QUIC.pdf

## Slide 17: Protocol Standardization
Most widely used protocols are defined in standards
Why standard?

## Slide 18: Internet Standardization Process
All standards of the Internet are published as RFC (Request for Comments)
  e.g., the SMTP protocol is specified in RFC821
  but not all RFCs are Internet Standards: http://zoo.cs.yale.edu/classes/cs433/cs433-2016-spring/readings/interestingrfcs.html

## Slide 19: Internet Standardization Process
All standards of the Internet are published as RFC (Request for Comments)
  e.g., the SMTP protocol is specified in RFC821
  but not all RFCs are Internet Standards: http://zoo.cs.yale.edu/classes/cs433/cs433-2017-fall/readings/interestingrfcs.html
A typical (but not the only) way of standardization:
  Internet draft
  RFC
  proposed standard
  draft standard (requires 2 working implementations)
  Internet standard (declared by Internet Architecture Board)
David Clark, 1992:
  We reject: kings, presidents, and voting. We believe in: rough consensus and running code.

## Slide 20: Outline
Administrative trivia’s
What is a network protocol?
A brief introduction to the Internet
  past (a brief history)
  present

## Slide 21: Prelude: Packet Switching and ARPANET
1957
  USSR launched Sputnik; US DoD formed Advanced Research Projects Agency (ARPA)
1961
  First paper by Len Kleinrock on packet switching theory
1964
  Paul Baran from RAND on design of packet switching networks
1965-1968
  ARPANET plan
  Bolt Beranek and Newman, Inc. (BBN), a small company, was awarded Packet Switch contract to build Interface Message Processors (IMPs)

## Slide 22: Internet 1.0: Initial ARPANET
1969
  ARPANET commissioned: 4 nodes, 50kbps

## Slide 23: Initial Expansion of the ARPANET
Dec. 1969
Mar. 1971
July 1970
Apr. 1972
Sept. 1972
RFC 527: ARPAWOCKY; RFC 602: The Stockings Were Hung by the Chimney with Care

## Slide 24: The Internet Becomes a Network of Networks
1970: ALOHAnet, the first packet radio network, developed by Norman Abramson, Univ of Hawaii, becomed operational
1973: Bob Kahn posed the Internet problem---how to connect ARPANET, packet radio network, and satellite network
1974: Vint Cerf, Bob Kahn published initial design of TCP (NCP) to connect multiple networks
  - 1978: TCP (NCP) split to TCP/IP
  - 1983: TCP (NCP) converted to TCP/IP (Jan. 1)

## Slide 25: Growth of the Internet
1981: BITNET (Because It’s Time NETwork) between CUNY and Yale
1986: NSF builds NSFNET as backbone, links 6 supercomputer centers, 56 kbps; this allows an explosion of connections, especially from universities
1987: 10,000 hosts
1988: Internet congestion collapse; TCP congestion control
1989: 100,000 hosts RFC 1121: Act One – The Poem WELCOME by Leonard Kleinrock We've gathered here for two days to examine and debate And reflect on data networks and as well to celebrate. To recognize the leaders and recount the path we took. We'll begin with how it happened; for it's time to take a look. Yes, the history is legend and the pioneers are here. Listen to the story - it's our job to make it clear. We'll tell you where we are now and where we'll likely go. So welcome to ACT ONE, folks.
Sit back - enjoy the show!!

## Slide 26: Internet 2.0: Web, Commercialization, Social Networking of the Internet
1990: ARPANET ceases to exist
1991: NSF lifts restrictions on the commercial use of the Net; Berners-Lee of European Organization for Nuclear Research (CERN) released World Wide Web
1992: 1 million hosts (RFC 1300: Remembrances of Things Past)
1998: Google was founded
2004: Facebook was founded
2006: Amazon AWS cloud computing
For a link of interesting RFCs, please see http://zoo.cs.yale.edu/classes/cs433/cs433-2017-fall/readings/interestingrfcs.html
For more on Internet history, please see http://www.zakon.org/robert/internet/timeline/

## Slide 27: Growth of the Internet in Terms of Number of Hosts
Number of Hosts on the Internet:
Aug. 1981 213
Oct. 1984 1,024
Dec. 1987 28,174
Oct. 1990 313,000
Jan. 1993 1,313,000
Jan. 1996 9,472,000
Jan. 1999 43,218,000
Jan. 2002 147,344,723
Jan. 2005 317,646,084
Jan. 2007 433,193,199
Jan. 2010 732,740,444
Jan. 2013 963,518,598
Jan. 2016 1,048,766,623
Jan. 2017 1,062,660,523
CAIDA router
level view
http://ftp.isc.org/www/survey/reports/current/

## Slide 28: Internet 3.0: Always-Connected, Virtualized Life
  Office
  Shopping
  Education
  Entertainment
  Environment
  => Virtual workspace
  => Online shopping
  => Remote education
  Online media/games
  Internet of things

## Slide 29: Outline
Administrative trivia’s
What is a network protocol?
A brief introduction to the Internet
  past
  present

## Slide 30: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet
  Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
data center

## Slide 31: Access: Fiber to the x
http://en.wikipedia.org/wiki/Fiber_to_the_x
Notes: the common form of gigabit Ethernet (1Gbit/s) runs over relatively economical category 5e, category 6, or augmented category 6 unshielded twisted-pair copper cabling but only to 300 ft (91 m). However, 1Gbit/s ethernet over fiber can easily reach tens of miles.

## Slide 32: Access: Fiber to the Premises (FTTP)
Deployed by Verizon, AT&T, Google
One of the largest comm. construction projects
Notes: Average US:
down: 5.8 MBps
Up: 1.2 Mbps
Google fiber:
Cost: $300/customer
http://en.wikipedia.org/wiki/Fiber_to_the_x
http://www.telecompetitor.com/google-ftth-invades-texas-with-austin-the-next-stop-for-google-fiber/
http://www.youtube.com/watch?v=6uZVqPuq81c

## Slide 33: FTTP Architecture
Notes: http://en.wikipedia.org/wiki/Fiber_to_the_x

## Slide 34: FTTP Architecture
Optical Network Terminal (ONT) box outside dwelling or business
Fiber Distribution Terminal (FDT) in poles or pedestals
Fiber Distribution Hub (FDH) at street cabinet
Optical Line Terminal (OLT) at central office

## Slide 35: FTTP Architecture: To Home

## Slide 36: FTTP Architecture: Fiber Distribution Terminal (FDT)

## Slide 37: FTTP Architecture: Central to Fiber Distribution Hub (FDH)
- Backbone fiber ring on
primary arterial streets
(brown)
- Local distribution fiber
plant (red) meets backbone
at cabinet
FDH

## Slide 38: Access: DSL
Compared with FTTP, copper from cabinet (DSLAM) to home
DSLAM

## Slide 39: Access: Wireless
https://x.company/loon/

## Slide 40: Access: Wireless
https://www.theguardian.com/technology/2016/nov/17/elon-musk-satellites-internet-spacex

## Slide 41: Campus Network
tier-1
Internet
CE
Tier-1
F1 (Firewall)
S1
LB1 (Load balancer)
IPS1 (Intrusion prevention)
F2
S2
LB2
IPS2
S3
S4
VLAN 300
VLAN 400
Tier-2
VLAN 100
R1
S5
IPS3
S6
VLAN 200
Tier-3
Logger

## Slide 42: Data Center Networks
http://www.dailymail.co.uk/sciencetech/article-3369491/Google-s-plan-world-Search-engine-build-half-billion-dollar-data-center-US.html

## Slide 43: Data Center Networks
http://www.dailymail.co.uk/sciencetech/article-3369491/Google-s-plan-world-Search-engine-build-half-billion-dollar-data-center-US.html
Notes: http://www.cse.wustl.edu/~jain/cse570-13/ftp/m_03dct.pdf

## Slide 44: Foundation of Data Center Networks
2
n
1
n
1
2

## Slide 45: Foundation of Data Center Networks: Clos Networks
https://en.wikipedia.org/wiki/Clos_network
Q: How big is m so that each new call can be established w/o moving current calls?
433/533 Labor day problem: If you can move existing calls, it is only m >= n.
Notes: Strict-sense nonblocking Clos networks (m ≥ 2n−1): the original 1953 Clos result[edit]
If m ≥ 2n−1, the Clos network is strict-sense nonblocking, meaning that an unused input on an ingress switch can always be connected to an unused output on an egress switch, without having to re-arrange existing calls. This is the result which formed the basis of Clos's classic 1953 paper. Assume that there is a free terminal on the input of an ingress switch, and this has to be connected to a free terminal on a particular egress switch. In the worst case, n−1 other calls are active on the ingress switch in question, and n−1 other calls are active on the egress switch in question. Assume, also in the worst case, that each of these calls passes through a different middle-stage switch. Hence in the worst case, 2n−2 of the middle stage switches are unable to carry the new call. Therefore, to ensure strict-sense nonblocking operation, another middle stage switch is required, making a total of 2n−1.
If m ≥ n, the Clos network is rearrangeably nonblocking, meaning that an unused input on an ingress switch can always be connected to an unused output on an egress switch, but for this to take place, existing calls may have to be rearranged by assigning them to different centre stage switches in the Clos network.[3] To prove this, it is sufficient to consider m = n, with the Clos network fully utilised; that is, r×n calls in progress. The proof shows how any permutation of these r×n input terminals onto r×n output terminals may be broken down into smaller permutations which may each be implemented by the individual crossbar switches in a Clos network with m = n.
The proof uses Hall's marriage theorem[4] which is given this name because it is often explained as follows. Suppose there are r boys and r girls. The theorem states that if every subset of k boys (for each k such that 0 ≤ k ≤ r) between them know k or more girls, then each boy can be paired off with a girl that he knows. It is obvious that this is a necessary condition for pairing to take place; what is surprising is that it is sufficient.
In the context of a Clos network, each boy represents an ingress switch, and each girl represents an egress switch. A boy is said to know a girl if the corresponding ingress and egress switches carry the same call. Each set of k boys must know at least k girls because k ingress switches are carrying k×n calls and these cannot be carried by less than k egress switches. Hence each ingress switch can be paired off with an egress switch that carries the same call, via a one-to-one mapping. These r calls can be carried by one middle-stage switch. If this middle-stage switch is now removed from the Clos network, m is reduced by 1, and we are left with a smaller Clos network. The process then repeats itself until m = 1, and every call is assigned to a middle-stage switch.

## Slide 46: Data Center Networks: Fat-tree Networks
K-ary fat tree: three-layer topology (edge, aggregation and core)
  k pods w/ each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
    each edge switch connects to k/2 servers & k/2 aggr. switches
    each aggr. switch connects to k/2 edge & k/2 core switches
  (k/2)2 core switches: each connects to k pods
http://www.cs.cornell.edu/courses/cs5413/2014fa/lectures/08-fattree.pdf
Q: How large a network can k-ary support using k-port switches?
Notes: K^3/4
http://www.fiber-optic-tutorial.com/100g-switch-price-and-configuration.html
http://web.stanford.edu/class/ee384y/Handouts/clos_networks.pdf
https://en.wikipedia.org/wiki/Clos_network

## Slide 47: Data Center Networks
For example, Google Jupiter at 1 Pbits/sec bisection bw: 100,000 servers at 10G each
http://conferences.sigcomm.org/sigcomm/2015/pdf/papers/p183.pdf
http://googlecloudplatform.blogspot.com/2015/06/A-Look-Inside-Googles-Data-Center-Networks.html
Notes: http://web.stanford.edu/class/ee384y/Handouts/clos_networks.pdf
https://en.wikipedia.org/wiki/Clos_network

## Slide 48: Recall: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access, e.g.,
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet, Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
data center

## Slide 49: Yale Internet Connection
cicada:~% traceroute www.tsinghua.edu.cn
1 college.net.yale.internal (172.28.201.65) 1.440 ms 1.227 ms 1.453 ms
2 10.1.1.13 (10.1.1.13) 1.359 ms 1.153 ms 1.173 ms 3 level3-10g-asr.net.yale.internal (10.1.4.40) 2.786 ms 6.110 ms 2.547 ms 4 cen-10g-yale.net.yale.internal (10.1.3.102) 2.646 ms 3.242 ms 2.576 ms 5 * * * 6 enrt064hhh-9k-te0-3-0-5.net.cen.ct.gov (67.218.83.254) 5.169 ms 3.797 ms 6.891 ms 7 198.71.46.215 (198.71.46.215) 3.615 ms 3.742 ms 3.931 ms 8 et-10-0-0.1180.rtsw.newy32aoa.net.internet2.edu (198.71.46.214) 6.661 ms 6.532 ms 6.310 ms 9 et-4-0-0.4079.sdn-sw.phil.net.internet2.edu (162.252.70.103) 8.658 ms 8.714 ms 8.666 ms 10 et-1-1-0.4079.rtsw.wash.net.internet2.edu (162.252.70.119) 11.787 ms 30.111 ms 11.900 ms 11 et-8-1-0.4079.sdn-sw.ashb.net.internet2.edu (162.252.70.62) 12.428 ms 16.654 ms 15.862 ms 12 et-7-1-0.4079.rtsw.chic.net.internet2.edu (162.252.70.61) 28.898 ms 28.999 ms 28.908 ms 13 et-3-1-0.4070.rtsw.kans.net.internet2.edu (198.71.47.207) 40.084 ms 39.958 ms 39.695 ms 14 et-8-0-0.4079.sdn-sw.denv.net.internet2.edu (162.252.70.10) 50.195 ms 50.562 ms 50.258 ms 15 et-4-1-0.4079.rtsw.salt.net.internet2.edu (162.252.70.9) 59.707 ms 60.261 ms 59.762 ms 16 et-7-0-0.4079.sdn-sw.lasv.net.internet2.edu (162.252.70.30) 67.555 ms 67.539 ms 67.312 ms 17 et-4-1-0.4079.rtsw.losa.net.internet2.edu (162.252.70.29) 72.419 ms 72.428 ms 72.376 ms ...

## Slide 50: Internet2
\
http://noc.net.internet2.edu/i2network/maps-documentation/maps.html#Internet2 Combined Infrastructure Network Map

## Slide 51: Internet2
http://atlas.grnoc.iu.edu/atlas.cgi?map_name=Internet2%20IP%20Layer

## Slide 52: Yale Internet Connection
Try traceroute from Yale to
www.microsoft.com
www.facebook.com
www.amazon.com
www.google.com

## Slide 53: Qwest Backbone Map
Qwest (CentryLink) Network Maps
http://www.centurylink.com/business/resource-center/network-maps/
http://www.centurylink.com/business/asset/network-map/ip-mpls-network-nm090930.pdf

## Slide 54: Level3 Network Map
http://www.level3.com/-/media/files/maps/en-network-services-level-3-network-map.pdf

## Slide 55: Internet ISP Connectivity
Roughly hierarchical
  Divided into tiers
  Tier-1 ISPs are also called backbone providers, e.g., AT&T, Verizon, Sprint, Level 3, Qwest
An ISP runs (private) Points of Presence (PoP) where its customers and other ISPs connect to it
ISPs also connect at (public) Internet Exchange Point (IXP)
  public peering
http://en.wikipedia.org/wiki/List_of_Internet_exchange_points_by_size

## Slide 56: Outline
Administrative trivia’s
What is a network protocol?
A brief introduction to the Internet
  past
  Present
    topology
    traffic

## Slide 57: Internet (Consumer) Traffic
Notes: http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white_paper_c11-481360.pdf

## Slide 58: Internet Traffic in Perspective
640K ought to be enough for anybody.

## Slide 59: Outline
Administrative trivia’s
What is a network protocol?
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps

## Slide 60: Scale
“Developers who have worked at the small scale might be asking themselves why we need to bother when we could just use some kind of out-of the-box solution. For small-scale applications, this can be a great idea. We save time and money up front and get a working and serviceable application. The problem comes at larger scales—there are no off-the-shelf kits that will allow you to build something like Amazon... There’s a good reason why the largest applications on the Internet are all bespoke creations: no other approach can create massively scalable applications within a reasonable budget.”
http://www.evontech.com/symbian/55.html

## Slide 61: Largest Internet Sites in U.S.
https://www.quantcast.com/top-sites
Notes: http://www.comscore.com/Insights/Press_Releases/2013/8/comScore_Media_Metrix_Ranks_Top_50_U.S._Web_Properties_for_July_2013

## Slide 62: General Complexity
Complexity in highly organized systems arises primarily from design strategies intended to create robustness to uncertainty in their environments and component parts.
  Scalability is robustness to changes to the size and complexity of a system as a whole.
  Evolvability is robustness of lineages to large changes on various (usually long) time scales.
  Reliability is robustness to component failures.
  Efficiency is robustness to resource scarcity.
  Modularity is robustness to component rearrangements.
David Meyer

## Slide 63
Core: Simple Forwarding to Network Functions
Modern networks contain diverse types of equipment beyond simple routing/forwarding
Source: [Sherry, et. al SIGCOMM’12]
Small: <=1k hosts; Medium: 1k-10k; Large: 10k-100k; Very Large: >= 100k
Enterprise networks

## Slide 64: Centralized vs Decentralized (Price of Anarchy)
Autonomous (“Selfish”) App: Assume each link has a latency function le(x): latency of link e when x amount of traffic goes through e:
s
t
l(x) = 1
l(x) = x
total traffic

## Slide 65: Autonomous (“Selfish”) App
Braess’s paradox
Notes: Every increase of 20 ms in latency leads to 1% drop in click-through rate
E-commerce abandonment zone:
  33% users will abandon a site takes longer than 4 sec [Jupiter]

## Slide 66: Decentralized (“Selfish”) Users
2
0
3
1
2 0
2 3 0
1 2 0
1 0
3 1 0
3 0
4
3
preferred
less
preferred

## Slide 67: Decentralized (“Selfish”) Users
2
0
3
1
2 3 0
2 0
1 2 0
1 0
3 1 0
3 0
4
3
preferred
less
preferred

## Slide 68: Distributed vs Centralized
Distributed computing is hard, e.g.,
  FLP Impossibility Theorem
  Arrow’s Impossibility Theorem
Achieved good design for only few specific tasks (e.g., state distribution, leader election). Hence, a trend in networking is Software Defined Networking, which is a way of moving away from generic distributed computing, by focusing on utilizing the few well-understood primitives, in particular logically centralized state.

## Slide 69: What Will We Cover?
A tentative schedule is posted at class schedule page
Network architecture and design principles
  Layered network arch; e2e principle
Application architecture and design principles
  application paradigms; high performance network app.
  HTTP/Web, Email, DNS, P2P, Blockchain, Content distribution
Transport
  transport services
  reliability; distributed resource allocation; primal-dual
  transport protocols: TCP/UDP

## Slide 70: What Will We Cover?
Network and link layers
  distributed, asynchronous, autonomous routing algorithms; scalable router design; IP/IPv6; mobile IP; cellular networks
  multiple access; queueing analysis; capacity analysis
  Cloud and data center design
Network security
  security primitives; BAN logic, SSL

## Slide 71: Summary
Course administration
A protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of a message or other events.
The past:
  facts:
    The Internet started as ARPANET in late 1960s
    The initial link bandwidth was 50 kbps
    The number of hosts at the end of 1969 was 4
  some implications of the past:
    ARPANET is sponsored by ARPA 
    The initial IMPs were very simple 
    Many networks 
Current:
  The number of hosts connected to the Internet is around 1 billions
  The backbone speed of the current Internet is about 40/100 Gbps
  The Internet is roughly hierarchical where ISPs interconnect at PoP and IXP
  Needs to handle scale, complexity, decentralization, security
design should survive failures
  need a network to connect networks
keep the network simple

## Slide 72: Preview
We have only looked at the topology/connectivity of the Internet
  a communication network is a mesh of interconnected devices
A fundamental question: how is data transferred through a network?

## Slide 73: Backup Slides

## Slide 74: Access: Cable
Fiber node: 500 - 2K homes
Distribution hub: 20K - 40 K homes
Regional headend: 200 K - 400 K homes
Also called Hybrid Fiber-coaxial Cable (HFC)
Notes: http://en.wikipedia.org/wiki/Hybrid_fibre-coaxial

## Slide 75: Northern CrossRoads (NoX) Aggregation Point (AP)
http://www.uis.harvard.edu/emerging_technologies/Northern_Crossroads_Map.gif

## Slide 76
http://www.oregon-gigapop.net/images/OregonGigapop2.gif