## Slide 1: Inside a Datacenter Hardware and Software Architecture
Wei Bai
Microsoft Research Redmond
Guest Lecture, Computer Networks @ Xiamen University
Notes: Self introduction

## Slide 2: Disclaimer
The opinions in this talk are my own.
Datacenter architecture is a very large topic. In this talk, I will focus on networking and briefly discuss storage and compute.
I will use many Microsoft products and technologies as examples in this talk. But general concepts should be able to be applied to other companies as well.
Material with thanks to Mark Russinovich, Albert Greenberg, Dave Maltz, Marcus Fontoura, Daniel Firestone, Costin Raiciu and others.
Notes: Before I talk about datacenters, I want to mention a few points here.

## Slide 3: What is a datacenter?
Notes: Let’s start with a fundamental question: what is a datacenter?

## Slide 4
A datacenter is a building, or a dedicated space used to house computer systems and associated components, such as telecommunications and storage systems.
Notes: According to Wikipedia, a datacenter is a facility used to house computer systems and associated components, such as power, cooling, telecommunications and storage systems. To some degree, you can think data center as a server room. But data center is super large.

## Slide 5: Microsoft @ Amsterdam

## Slide 6: Microsoft @ Quincy

## Slide 7
Notes: I use this figure to give you some sense of the physical size of a data center. This is an architecture rendering of one of our data center buildings. Note that we don’t really put any 747 in our data centers. But these two 747s give you some sense of how large the physical space is. A production data center can host 10s of thousands of machines.

## Slide 8
https://www.google.com/about/datacenters/locations/
https://aws.amazon.com/about-aws/global-infrastructure/
https://docs.microsoft.com/en-us/azure/networking/microsoft-global-network
https://datacenters.fb.com/
Notes: Given the trend of cloud computing and digital transformation, many companies are building a lot of data centers around the world to provide service to global users. Here I show four companies, meta, amazon, google and Microsoft. All these four companies have a significant amount of first-party workloads, for example, Facebook social networking, Amazon shopping, Google search, Bing search and Microsoft office 365. But except for meta, all the other three companies provide cloud computing services. This means that Amazon, Google and Microsoft’s data centers run a mix of first-party and third-party workloads.

## Slide 9: Physical Networking
How to connect servers within a datacenters?
How to connect different datacenters and Internet?
Notes: After talking about the basic knowledge of datacenters, let’s move to physical networking. In datacenter context, the physical networking needs to address two key problems.

## Slide 10: Traditional Data Center Topology (2008)
Core Switches
Aggregation Switches
Top of Rack Switches
Racks of Servers
Notes: Data center network topology and architecture has become a very hot topic since 2008. At that time, I was still a high school student. This slide gives a figure of traditional DCN topology in 2008. Tens of servers are connected to a top of rack switch using 1Gbps links. Every top of rack switch is connected to an aggregation switch using a 10Gbps link. An aggregation switch can be connected to multiple core switches.

## Slide 11: Problems in Traditional Solutions
Lack robustness
  Aggregation switch failures wipe out several racks
Poor performance
Oversubscription = max_host_throughput / worst_case_throughput
  Typical oversubscription ratio 4:1, 8:1, 10:1
Expensive
  7K for 48-port Gigabit switch
  700K for 128-port 10Gigabit switch
Notes: So what are the problems of the traditional solution?

## Slide 12: Ideal Datacenter Network Topology
Offer full-bisection bandwidth
  Over-subscription ratio of 1:1
  Worst case: every host can talk to every host at line rate!
Is fault tolerant
Is cheap
Notes: So how does an ideal datacenter network topology look like?

## Slide 13: The Fat Tree [Al-Fares et al, SIGCOMM 2008]
Inspired from the telephone networks of the 50’s – Clos networks
Use cheap, commodity switches – all switches are the same
Lots of redundancy
Single parameter to describe the topology:
  K – the number of ports in a switch
Notes: To realize the ideal datacenter network topology, some researchers from UCSD design a network called fat tree.

## Slide 14: Fat Tree Topology
𝐾^3/4
Core Switches
Aggregation Switches
Edge Switches
Servers
Notes: This figure shows a fat tree with K = 4. This means that every switch has 4 ports. There are three tiers of switches.

## Slide 15: Fat Tree Topology
𝐾^3/4
Core Switches
Aggregation Switches
Edge Switches
Servers
Notes: Fat tree has some basic properities.

## Slide 16: The Fat Tree Topology has paths between any two endpoints
𝐾^3/4
Core Switches
Aggregation Switches
Edge Switches
Servers
Notes: This figure shows a fat tree with K = 4.

## Slide 17: Routing: how to use these paths
Layer 2: Spanning Tree Protocol (STP)
  STP does not offer multiple paths
  What about L2 broadcasts? (e.g., ARP)
Layer 3: Equal Cost Multipath Routing (ECMP)
  When there are multiple shortest paths, pick one “randomly”
  Hash packet header to choose a path
  All packets of the same flow go on the same path
Why not use per-packet ECMP?
Notes: So how to use these paths.
First option ..
Second option is ..

## Slide 18: Other Topologies
Jellyfish [Singla et al, NSDI 2012]
BCube [Guo et al, SIGCOMM 2009]
Servers
Switches

## Slide 19: Reconfigurable Topologies
Optical Circuit Switching
2 circuits
Notes: So far we have talked several topologies, fat tree, vl2. All these topologies are static.

## Slide 20: Reconfigurable Topologies
Time Slot = 1

## Slide 21: Reconfigurable Topologies
Time Slot = 2

## Slide 22: Reconfigurable Topologies
Time Slot = 3

## Slide 23
What topologies are used in practice?

## Slide 24: Network Architecture of an Azure Region
Server
Tier 0
Tier 1
Tier 2
Regional Hub
Data Center
Cluster
Notes: This figure gives the topology of an Azure region. Green ones are servers. Then there are four tiers of switches, T0, T1, T2 and RH.

## Slide 25: Regional Spine Architecture
Customers want the Cloud to be infinitely scalable – how to create that illusion?
Regional network gateway
Massively parallel, hyper scale
Space and power protected
Data centers
Only contains server racks, DC network
RNGs are sized to support growing the region by adding data centers
Introducing: Regions
Contiguous geographical area up to roughly 100km in diameter (2.0ms RTT)

## Slide 26: Microsoft Global Network
61
Azure regions
175k+
miles of fiber + subsea cables
185+
Network edge sites
200+
Express route partners
20k+
peering connections
Notes: Microsoft owns and operates one of the largest global networks on the planet. This global and sophisticated architecture, spanning more than 175,000 miles of fiber, connects our datacenters and customers. Connecting our Microsoft data centers across 61 regions and large mesh of edge-nodes placed around the world, our global network offers both the availability, capacity, and the flexibility to meet any demand. These edge-nodes, all interconnected to more than 4,600 unique Internet partners (peers) through 20,000+ connections in more than 185 locations, provide the foundation of our interconnection strategy. Our edge PoP expansion mission is to reach every human on the planet within 25 milliseconds. Our policy is to establish peering directly in market with the local providers and carrying the traffic across our secure global backbone network to exit close to the user so that we control the quality over as much of the path as possible.

## Slide 27: Microsoft Azure Networking
Enterprise DC/Corpnet
Consumers
Regional Network
Microsoft Wide Area Network
Edge
ExpressRoute
CDN
Enterprise, SMB, mobile
Azure Region ‘A’
Azure Region ‘B’
Regional Network
Regional Network
Regional Network
Internet
Exchanges
Cable
Carrier

## Slide 28: Google uses optical circuit switching (OCS) switches to reconfigure networks between aggregation blocks

## Slide 29: Virtual Networking
How to enable multi-tenancy on a shared network fabric?

## Slide 30: Customers only see Virtual Networks (VNets)
10.0.0.0/24
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.0/24
10.0.0.1
10.0.0.2
10.0.0.3
Internet
Internet
Public IP addresses
Public IP addresses
Private Network
Private Network

## Slide 31: Key Mechanism: Packet Encapsulation
Server1: 1.1.1.5
Yellow VM1
10.1.1.2
Green VM1
10.1.1.2
Azure VMSwitch
Server2: 1.1.1.6
Red VM1
10.1.1.2
Green VM2
10.1.1.3
Azure VMSwitch
Src:10.1.1.2
Dst:10.1.1.3
Src:10.1.1.2
Dst:10.1.1.3
Policy lookup:
VM 10.1.1.3 is
on host with Physical Address
1.1.1.6
Packet is on
Green Vnet:
Decap
Virtual Network Controller
Src:1.1.1.5
Dst:1.1.1.6
GRE:Green
Src:10.1.1.2
Dst:10.1.1.3
L3 Forwarding Policy
Secure, intra-tenant networks
on shared infrastructure
Notes: Take a look at concrete policy
1st green vm wants to talk to 2nd green vm
Green in own addr space different than that the physical network runs on
When packet goes out, policy lookup in the 1st VM switch. Looks up the destination address. Encapsulates the packet, and delivers it to the 2nd switch
Decaps and delivers to the green VM
Just used this model to program secure intra-tenant networks on shared infrastructure

## Slide 32: Azure Software Defined Networking (SDN)
Management plane | Create a tenant
Control plane | Plumb tenant policies to VM switches
Data plane | VM switches apply policies to flows
Key to flexibility and scale is Host SDN

## Slide 33: Azure VM Switch: Virtual Filtering Platform
Virtual Filtering Platform (VFP) exposes a typed Match-Action-Table API to the agents/controllers
Key insight: Let controller tell switch exactly what to do with which packets
Host: 10.4.1.5
Tenant Description
VNet Description
VNet Routing Policy
ACLs
NAT Endpoints
Rule | Action
TO: 10.2/16 | Encap to GW
TO: 10.1.1.5 | Encap to 10.5.1.7
TO: !10/8 | NAT out of VNET
Rule | Action
TO: 79.3.1.2 | DNAT to 10.1.1.2
TO: !10/8 | SNAT to 79.3.1.2
Rule | Action
TO: 10.1.1/24 | Allow
10.4/16 | Block
TO: !10/8 | Allow
VNET
LB NAT
ACL
VM Switch
Controller
NIC
VM 1
10.1.1.2
Load Balance
Network Address Translation
Access Control List
Virtual Network

## Slide 34: Generic Flow Table (GFT) – A Fastpath
First-packet actions can be complex
Established-flow matches must be typed, predictable, and simple hash lookups
Rule | Action
TO: 10.2/16 | Encap to GW
TO: 10.1.1.5 | Encap to 10.5.1.7
TO: !10/8 | NAT out of VNET
NIC
VM Switch
First Packet
Subsequent Packets
Flow | Action
Flow | Action
Rule | Action
TO: 79.3.1.2 | DNAT to 10.1.1.2
TO: !10/8 | SNAT to 79.3.1.2
Rule | Action
TO: 10.1.1/24 | Allow
10.4/16 | Block
TO: !10/8 | Allow
VNET
LB NAT
ACL
Flow | Action
10.1.1.2:80 to 10.2.3.5:9876 | DNAT + Encap to GW
10.1.1.2:80 to 10.2.1.5:9876 | Encap to 10.5.1.7
10.1.1.2:6754 64.3.2.5:80 | SNAT to 79.3.1.2
Rule Lookups (Expensive)
Hash Lookups (Cheap)
VM 1
10.1.1.2

## Slide 35: Compute and Storage

## Slide 36: Virtual Machines in Azure
Type | Sizes | Description
General Purpose | B, Dsv3, Dv3, Dasv4, Dav4, DSv2, Dv2, Av2, DC, DCv2, Dpdsv5, Dpldsv5, Dpsv5, Dplsv5, Dv4, Dsv4, Ddv4, Ddsv4, Dv5, Dsv5, Ddv5, Ddsv5, Dasv5, Dadsv5 | Balanced CPU-to-memory ratio. Ideal for testing and development, small to medium databases, and low to medium traffic web servers.
Compute optimized | F, Fs, Fsv2, FX | High CPU-to-memory ratio. Good for medium traffic web servers, network appliances, batch processes, and application servers.
Memory optimized | Esv3, Ev3, Easv4, Eav4, Epdsv5, Epsv5, Ev4, Esv4, Edv4, Edsv4, Ev5, Esv5, Edv5, Edsv5, Easv5, Eadsv5, Mv2, M, DSv2, Dv2 | High memory-to-CPU ratio. Great for relational database servers, medium to large caches, and in-memory analytics.
Storage optimized | Lsv2, Lsv3, Lasv3 | High disk throughput and IO ideal for Big Data, SQL, NoSQL databases, data warehousing and large transactional databases.
GPU | NC, NCv2, NCv3, NCasT4_v3, ND, NDv2, NV, NVv3, NVv4, NDasrA100_v4, NDm_A100_v4 | Specialized virtual machines targeted for heavy graphic rendering and video editing, as well as model training and inferencing (ND) with deep learning. Available with single or multiple GPUs.
High performance compute | HB, HBv2, HBv3, HC, H | Our fastest and most powerful CPU virtual machines with optional high-throughput network interfaces (RDMA).

## Slide 37: Compute-Storage Disaggregation
CPU
MEM
CPU
CPU
MEM
MEM
Compute Server
Storage Server
NIC
NIC
Datacenter Network
What are benefits of resource disaggregation?

## Slide 38: Virtual Machine (VM) Allocation
Resource constraints
  Sum of recourses of all VMs on a node cannot exceed server resources (CPU, memory, disk, network, …) -> Bin-Packing
Failure domain constraints
  VMs of the same tenant must be spread across many failure domains
Co-location constraints
  Certain types of VMs cannot be co-located together

## Slide 39: Azure Storage Architecture
Geo replication
Blob
Queue
File
SMB
Storage Stamp
LB
Partition Layer
Front-Ends
Stream Layer (DFS)
Intra-stamp replication
Storage Stamp
LB
Partition Layer
Front-Ends
Stream Layer (DFS)
Intra-stamp replication
Blob
Queue
File
SMB

## Slide 40: Datacenter Innovations
1% saving or improvement means a lot at cloud scale
0.01% downtime also means a lot for a cloud

## Slide 41: Azure SmartNIC: accelerate VM switch
VM
VFP
Southbound API
GFT Offload API (NDIS)
VMSwitch
Northbound API
GFT
Table
First Packet
GFT Offload Engine
100G
QoS
Crypto
RDMA
GFT
Transposition
Engine
REWRITE
SLB Decap
SLB NAT
VNET
ACL
Metering
Controller
Controller
Controller
Encap
SmartNIC
DNAT
Decap
Allow
Meter
Rule | Action
* | Meter
Rule | Action
* | Allow
Rule | Action
* | Rewrite
Rule | Action
* | DNAT
Rule | Action
* | Decap
Flow | Action
1.2.3.1->1.3.4.1, 62362->80 | Decap, DNAT, Rewrite, Meter
Flow | Action
1.2.3.1->1.3.4.1, 62362->80 | Decap, DNAT, Rewrite, Meter

## Slide 42: Remote Direct Memory Access (RDMA)
Memory
Buffer A
Write local buffer at address A to remote buffer at address B
Buffer B is filled
DMA
Application
Application
Memory
Buffer B
DMA
Requester
Responder
Allocate
Allocate
  RDMA bypasses host OS stack
   frees host CPU, lowers latency
Notes: Let’s start with basic concept of RDMA. I think many of you know DMA, direct memory access. This is a feature that allows certain hardware subsystems to access main memory independently of CPU. RDMA is essentially remote DMA that crosses different machines.
In this example, there are two hosts which are connected by the network. The requester application tells its NIC ‘hey, can you send data I store in local buffer A to a remote buffer B’.
[click]
The requester’s NIC fetches data from host memory using DMA without involvement of CPU, assemble data into packets, and [click] send packets to the destination NIC through the network.
[click]
Then destination NIC de-assemble packets to get data, writes data to the memory B, and tells the responder application “Hey, someone writes something to your buffer B”
[click]
This data exchange process does not involve network stack running in OS kernel, thus freeing CPU cores. Compared to OS network stack, NIC hardware can provide much lower processing latency and better throughput.

## Slide 44: New CPUs
AWS Arm-based Graviton2 CPU

## Slide 45: Next Generation Datacenter Architectures
Compute Pool
Accelerator Pool
SSD Pool
DRAM Pool
Next Generation Network Interconnect

## Slide 46: Aquila: A Unified, Low-latency Datacenter Network

## Slide 47: Sustainable Datacenters
Boiling liquid carries away heat generated by computer servers at a Microsoft datacenter
An on-site solar energy array at the Google data center campus in Belgium

## Slide 48: Project Natick: Underwater Datacenters
Notes: 864 servers

## Slide 49: Customer Benefits
Reduce the cost of cooling by leveraging the natural sea temperature.
Benefit from offshore renewable energy sources (e.g., wave and tidal power) that could be truly zero emission.
Made from fully recyclable materials.
Reduce the latency by locating datacenters closer to customers.

## Slide 50: Datacenters in Space

## Slide 51: Thank You!
Interested in opportunities at Microsoft?
Please drop me an email webai@microsoft.com