## Slide 1: You Don't Need a Centralized Verifier: Toward Scalable Data Plane Checking via Distributed, On-Device Verification
Qiao Xiang1, Chenyang Huang1, Ridi Wen1, Yuxin Wang1, Xiwen Fan1,
Alan Liu2, Linghe Kong3, Dennis Duan4, Franck Le5, Wei Sun6
1Xiamen University, 2University of Maryland, 3Shanghai Jiao Tong University, 4Yale University, 5IBM T.J. Watson Research Center, 6UT Austin
June 2023, Hong Kong, China, ACM APNet'23

## Slide 2: Background
Modern networks are
  increasingly more complex
  outages increasingly more costly
Source: http://groups.geni.net/geni/chrome/site/thumbnails/wiki/TangoGENI/OF-VLAN3715_1000.jpg

## Slide 3: Network Verification: Powerful Tool to Check Network Forwarding Behavior
Control Plane
execute
Control plane verification
Batfish [NSDI'15]
Bagpipe [OOPSLA'16]
Minesweeper [SIGCOMM'17]
Bonsai [SIGCOMM'18]
Hoyan [SIGCOMM'21]
…
config
config
config
Data Plane
Data plane verification
HSA [NSDI'12]
Veriflow [NSDI'13]
Atomic Predicates [ICNP'13]
APKeep [NSDI'20]
Flash [SIGCOMM'22]
…
FIB
FIB
FIB
Notes: Traditional operators don’t use verification
That may be changing with new tools like HSA, Veriflow
Still, there is simulation in the mix, because the control plane will be simulated

## Slide 4: Why Study Data Plane Verification?
Data plane is the ground truth of actual forwarding behavior
Q: Why CP verification fails to catch this?
A: ACL/routing configurations pass control plane verification, but with a different input from the actual network

## Slide 5: How Does DPV Usually Work?
A (cluster of) server(s) as a centralized verifier
  Collect the data plane (e.g., FIB/ACL) from routers/switches through management network
  Run computation-intensive, memory-intensive computation to verify the network data plane
Verifier
Management
Network
FIB/ACL
FIB/ACL
FIB/ACL
FIB/ACL

## Slide 6: Issues of Centralized DPV
Need a highly-available management network
  Incomplete DP, inconclusive result
Verifier becomes performance bottleneck
  Larger network, more computation power
Verifier becomes single PoF
  Verifier fails, no result
Out-of-band verification
  Slow reaction to errors
Verifier
Management
Network
FIB/ACL
FIB/ACL
FIB/ACL
FIB/ACL

## Slide 7: Our Proposal: Distributed, On-Device Verification
Basic idea: offload verification to distributed computations on network devices
Benefits:
  Minimize the requirement of management network
    Once configured, run automatically
  No performance bottleneck
    More network devices, more verifiers
  No single PoF
    Device malfunction equals a network error
  Verification-as-a-service for vendors
    Support flexible in-situ fast reroute
Verifier
Management
Network
On-device tasks
On-device tasks
On-device tasks
On-device tasks
FIB/ACL
FIB/ACL
FIB/ACL
FIB/ACL

## Slide 8: Distributed, On-Device Verification: Challenges
Challenge 1: How to specify the invariants to check?
  Most DPV tools only check a fixed set of invariants (e.g., reachability, loop-free and blackhole-free)
Challenge 2: How to make the on-device tasks lightweight?
  Switches/routers have low-end CPU and already run multiple protocols (e.g., SNMP, OSPF and BGP)
Challenge 3: How to make devices exchange results correctly and efficiently?
  Distributed computing has its own issues (e.g., safety, liveness and consistency)

## Slide 9: Tulkun: A Generic, Distributed, On-Device DPV Framework
Network
Topology
Verification
Invariant
+
Verification Messages
DVNet
On-Device Tasks
Declarative Invariant Specification Language
Verification Planner
On-Device Verifiers
/ DV Protocol
C1:
Invariant specification
C2:
lightweight tasks decomposition
C3: collaborative verification

## Slide 10: A Running Example
Invariant: all packets entering the network from S with a destination IP in 10.0.0.0/23 must be delivered to D in a simple path waypointing W.
Topology:
10.0.0.0/23
S
A
B
C
D
W

## Slide 11: Step 1: Invariant Specification
Invariant: all packets entering the network from S with a destination IP in 10.0.0.0/23 must be delivered to D in a simple path waypointing W.
(dstIP = 10.0.0.0/23, [S], S .* W .* D and loop_free, "exist >=1")
Tulkun program:
packet space
ingress
set of
valid paths
number of
valid paths

## Slide 12: Step 2: From Invariant and Topology to DVNet
(dstIP = 10.0.0.0/23, [S],
S .* W .* D and loop_free, "exist >=1")
Invariant:
Topology:
S1
B1
C2
B2
C1
W2
D1
W1
W3
A1
10.0.0.0/23
S
A
B
C
D
W
DVNet: a DAG representing all valid paths in the network
X (DFA multiplication)

## Slide 13: Step 3: From Verification in Network to Counting in DVNet
Each node counts # of downstream paths provided by data plane in reverse topological order
S1
B1
C2
B2
C1
W2
D1
W1
W3
A1
[(P1, 1)]
P1: dstIP=10.0.0.0/23
P2: dstIP=10.0.0.0/24
P3: dstIP=10.0.1.0/24
[(P1, 0)]
[(P1, 1)]
[(P1, 0)]
[(P1, 0)]
[(P1, 1)]
[(P1, 1)]
[(P1, 1)]
[(P2, [0, 1]),
(P3, 1)]
[(P2, [0, 1]),
(P3, 1)]
Error found!
10.0.0.0/23
S
A
B
C
D
W

## Slide 14: Step 4: Distributed, Event-Driven, On-Device Counting
Counting in DVNet can be naturally decomposed and executed at corresponding devices
S1
B1
C2
B2
C1
W2
D1
W1
W3
A1
[(P1, 1)]
P1: dstIP=10.0.0.0/23
P2: dstIP=10.0.0.0/24
P3: dstIP=10.0.1.0/24
[(P1, 0)]
[(P1, 1)]
[(P1, 0)]
[(P1, 0)]
[(P1, 1)]
[(P1, 1)]
[(P1, 1)]
[(P2, [0, 1]),
(P3, 1)]
[(P2, [0, 1]),
(P3, 1)]
10.0.0.0/23
S
A
B
C
D
W
fwd(ALL, {W})
[(P1, 1)]
[(P1, 0)]
[(P1, 1)]
[(P1, 1)]

## Slide 15: Tulkun: Extensions
Data plane with packet transformation
  Sub-pub mechanism added to on-device tasks
Message-free local verification
  All-path-availability: any task finding error equals network error (Microsoft RCDC [SIGCOMM'19] becomes a special case)
Fault-tolerant invariant (e.g., shortest path under k-link-failure)
  Precomputing fault-tolerant DVNet
Incremental deployment
  device/vm interconnect + partition

## Slide 16: Implementation
A total ~8K lines of Java code
On-device verifier runs on SONiC and ONL
  Requirement: JRE
SONiC HLD proposal
  https://github.com/sonic-net/SONiC/pull/948
  To be open-sourced upon publication

## Slide 17: Experiment 1: Functionality Demonstration
6-switch testbed: 4 Mellanox, 1 UfiSpace, 1 Edgecore
Demo scenarios:
  Waypoint reachability (running example)
  Multicast
  Anycast
  Different-ingress consistent reachability
  All-shortest-path availability
Demo videos: http://distributeddpvdemo.tech/
Interactive demos: https://distributeddpchecking.com:8443
S
A
B
C
D
W

## Slide 18: Experiment 2: Verifying Internet2
9-switch testbed with Internet2 topology: 4 Mellanox, 4 P4, 1 Edgecore whitebox
Inject propagation latency among switches based on device location in topology
Public Internet2 data plane dataset
Snapshot, all-rule verification: finish verifying all-pair loop-free, blackhole-free, <=x+2-hop reachability in 0.99 second
10,000 incremental, per-rule-update verification: 80% finish in <=5.42ms

## Slide 19: Experiment 3: Large-Scale Simulations
13 datasets spanning campus networks, WAN and DCN
Compare with 5 centralized DPV tools: Veriflow [NSDI'13], Deltanet [NSDI'17], AP [ICNP'13], APKeep [NSDI'20], Flash [SIGCOMM'22]

## Slide 20: Simulation: Snapshot Verification
Tulkun accelerate snapshot verification by up to 1250x

## Slide 21: Simulation: 10,000 Incremental Per-Rule-Update Verification
Tulkun verifies at least 73% of rule updates in less than 10 ms and up to 2355x faster than SOTA in 80% quantile

## Slide 22: Experiment 4: Microbenchmark on Commodity Switches
Initialization overhead (computing local equivalence classes)
  Memory 20 MB, CPU load 0.46，initalization in 1.75 s

## Slide 23: Experiment 4: Microbenchmark on Commodity Switches
Message processing overhead
  Memory 45 MB, CPU load 0.2, 90% messages processed in 4 ms

## Slide 24: Summary
Advantages of distributed DPV over centralized DPV:
  better scalability, no single PoF, verification-as-a-service for vendors
Tulkun design elements:
  declarative invariant specification language; planner via DVNet; on-device verifier and messaging protocol
Extensive evaluation using demo/testbed/simulation/microbenchmark: real-time, scalable in-network verification
Publications: ACM HotNets'22, ACM SIGCOMM'23
Open-source/demos：https://github.com/sonic-net/SONiC/pull/948
https://distributeddpchecking.com:8443/
http://distributeddpvdemo.tech/
For more information about Tulkun，reach out by email (qiaoxiang@xmu.edu.cn) or WeChat

## Slide 25: What Happens Next: Automating the Full Cycle of Network Configuration Management
Verification
Diagnosis
/Localization
Repair
DPV
Coral [HotNets'22]
[SIGCOMM'23]
Flash [SIGCOMM'22]
CPV
A-Graph [INFOCOM'21]
CCoral [WIP]
Diagnosis / Repair
Scalpel [APNet'23]
Interdomain
Configuration
Interdomain
Verification
IVeri [arXiv'21]
ICoral [WIP]
InCV [APNet'23]
Interdomain
Repair
IRepair [WIP]
Interdomain Synthesis
SDI [INFOCOM'20]

## Slide 26: XMU SNGroup
Young team
6 PhD students
20 graduate students
4 undergraduates
Fun research
Network and formal methods
Programmable networks
High-performance networks
Interpretable intelligent networks
Welcome to Visit Us!
SNGroup: sngroup.tech
Contact us: sngroup.xmu@outlook.com