## Slide 1: Diagnosing Distributed Routing Configurations Using Sequential Program Analysis
Rulan Yang1 , Xing Fang1, Lizhao You1, Qiao Xiang1, Hanyang Shao1, Gao Han1, Ziyi Wang1, Jiwu Shu1, 2, Linghe Kong3
1 Xiamen University, 2 Minjiang University, 3 Shanghai Jiao Tong University 2023/6/29

## Slide 2: Router configuration errors are common
Notes: network configuration errors are common, and it’s important to find them and fix them before the deployment.

## Slide 3
Detecting if configurations are erroneous:
What does network verification do?
Configurations
Results
reachability ?
waypoint ?
...
Notes: network verification tools can proactively check if the configurations are erroneous.
Check if some properties like reachability, waypoint hold for the configs

## Slide 4
Detecting if configurations are erroneous:
What does network verification do?
Configurations
Network model
translate the configuration to another representation
Verification tools | Network model they generate
Simulation-based tools (e.g., Batfish) | RIB/FIBs (i.e., The data plane)
Graph-based tools (e.g., ARC) | Abstraction graph
SMT-based tools (e.g., Minesweeper) | Logic formula
Notes: they first translate the config to another representation, some kind of network model.
Like simulation-based tools will concretely generate the RIBs of each router, that is the data plane,
and like SMT-based tools model both the config and network property as logic formula

## Slide 5
Detecting if configurations are erroneous: answer the YES/NO question
What does network verification do?
Configurations
Network model
Results
reachability √
waypoint ×
...
check if properties hold for the model
translate the configuration to another representation
Verification tools | Network model they generate | The way they verify properties
Simulation-based tools (e.g., Batfish) | RIB/FIBs (i.e., The data plane) | Data plane verification  Compute and verify the data plane
Graph-based tools (e.g., ARC) | Abstraction graph | Compute graph invariants
SMT-based tools (e.g., Minesweeper) | Logic formula | Check the satisfiability of the formula
Notes: Such as simulation based-tools, they compute and verify the data plane
SMT-based tools, they model the network and properties as a logic formula and check the satisfiability of the formula.
It is still up to operators to diagnosis and repair

## Slide 6: Why diagnosis is hard?
      Network is a (complex) distributed system
Property: S-B-D
S
A
B
D
Reality: S reaches D through “S-A-D”
B prefers A as the next-hop
([B, A, D])
([A, D])
([S, A, D])
add tag 1
match tag 1
set local-pref 130
Configuration errors on one router will lead to the property violation of other routers
Notes: But the root cause is that B was configured to

## Slide 7: Verification is not enough
Verification can tell us:
However, they cannot diagnose:
How do the configuration errors contribute to the results?
The error flow: s->a->d
The error result: false
The counter-example:
Batfish
Minesweeper
Notes: If we use verification tools to verify this network,
let’s see, the left one is the result return from Batfish, a state-of-the-art simulation-based tool, we can know that the flow will go through S-A-D,
and the right one is minesweeper’s output, we only know the true/false result, furthermore, MS doesn’t support AS-path regular expression.
but we still don’t know How do the configuration errors contribute to the results, it needs manual efforts.

## Slide 8: Key insight: understanding the distributed routing as a sequential program
Running the routing process
B
S
A
D
T0
T1
Distributed routing processes
Distributed network execution
Receive routes
Route selection
Send routes
Distributed routing is a program consisting of the three parts
…
…
…
8
[S, A, D]
[B, A, D]
[A, D]
[D]
receive ([A, D])
select ([A, D])
receive ([D])
select ([D])
send ([A, D])
receive ([A, D])
send ([D])
S
B
A
D
T1
…
…
send ([B, A, D])
receive ([D])
…
…
receive ([B, A, D])
Notes: We consider the execution trace is deterministic for the same network configuration.

## Slide 9: Key insight: understanding the distributed routing as a sequential program
Distributed network execution  The causal relationship graph (CRG)
Using (sender, receiver) and timestamp to capture the causal relationship
[S, A, D]
[B, A, D]
[A, D]
[D]
receive ([A, D])
select ([A, D])
receive ([D])
select ([D])
send ([A, D])
receive ([A, D])
send ([D])
S
B
A
D
T1
…
…
send ([B, A, D])
receive ([D])
…
…
receive ([B, A, D])
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
receive ([A, D])@S
receive ([B, A, D])@S
select ([A, D])@B
send ([B, A, D])@B
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
…
…
Notes: Next, I will introduce how we transform such distributed execution trace into a centralized, sequential program using causal relationships.
We know that receiving function will be called whenever a route comes, so we say that the incoming route is the cause of that function call, and then the router selects the best route, the best one will be downloaded to the RIB, and if there is any update of RIB, the new route in the RIB will be the input of receiving functions on other routing processes, and those are actions of the cause route.
So there exist causal relationships between them, and we use (receiver, sender) and timestamp to capture such relationships, which we called CRG.

## Slide 10: Key insight: understanding the distributed routing as a sequential program
Transforming the distributed program into a linear trace
topological traversal
or
…
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
…
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
…
receive ([D])@A
select ([D])@A
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
receive ([A, D])@S
receive ([B, A, D])@S
select ([A, D])@B
send ([B, A, D])@B
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
…
…
Notes: Then we can transform the distributed program into a sequential program using the CRG, it is to topologically traverse the graph to get the linear sequence.
Like this, or …
And we demonstrate that each topological traversal of the CRG will produce the same output.

## Slide 11: Analyzing the trace
Configurations are input to the program
Network properties are assertions that the program need to hold
Input: Configurations
assert Property == true
Diagnosis reasons about the execution
executing
reasoning
Verification executes the configurations
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
…
receive ([D])@A
select ([D])@A
Notes: So far, we get the sequential program,
The input of the program is configurations, verification is just executing it and output the data plane.
And the property we try to verify are some assertions at the end of the program
But Diagnosis needs reasoning, That is to analyze the program, to find why the program failed, and why it outputs the wrong dataplane.

## Slide 12: Analyzing the trace
Input: Configurations
assert Property == true
executing
reasoning
For observable errors (ones with traces that generate erroneous paths):
We diagnose errors by analyzing the data dependency
How erroneous paths were computed?
[S, A, D]
[B, A, D]
[A, D]
[D]
S
B
A
D
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
…
receive ([D])@A
select ([D])@A
Notes: We define observable errors are such errors that have erroneous paths, as the example shows.
We analyze the data dependency of these paths using data-flow analysis to know how erroneous paths were computed, and which part of the program contribute to them.

## Slide 13: Data-flow analysis using MUC&EI
Get the data dependency with explanation:
Minimal Unsatisfiable Core (MUC):
A minimal set of statements leading to the error
Error Invariants:
Key program states of statements
D(Static)->D(BGP)
D->A
A->S
A->B
D->B
B->S
D sent [D] to A and B
A received [D], selected it and sent it to S and B
B received [D] and [A, D], selected [A, D] since that B prefers A
S received [A, D] and [B, A, D], selected [A, D] since it has the shorter as-path length
send ([D])@D
receive ([D])@A
receive ([D])@B
receive ([A, D])@B
select ([A, D])@B
send ([B, A, D])@B
select ([D])@A
send ([A, D])@A
receive ([A, D])@S
receive ([B, A, D])@S
…
receive ([D])@A
select ([D])@A
Notes: The data-flow analysis is to explain why the program failed, the explanation consists of two parts.
First is MUC, here is the MUC of the example,
then we compute ei for the MUC, they are some transient program states that will eventually lead to the error state.
In this example, they explained why S chooses [S, A, D], …, then we know the modification of [B, A, D] is the configuration error.

## Slide 14: Data-flow analysis has limitations
Unobservable errors
Latent errors
S
A
B
D
()
()
()
D doesn’t redistribute the route to BGP process
S drops routes from both A and B
Property: S-*-D
Reality: There is no path from S to D
D(Static)
The trace:
(have exponential searching space)
(need repeated DF diagnosis)
Notes: Unfortunately, there are limitations of DFA,
let’s see this example.
…
there are two errors in this network

## Slide 15: Control-flow analysis using symbolic execution
…
…
…
Program
Collect more traces with their path conditions to analyze:
…
How to diagnose?
Correct execution path
Incorrect execution path
Errors
Differentiate these traces
…
A path condition is a predicate that a symbolic execution trace needs to hold
Notes: so we turn to CFA to get the control dependency of the program
Using symbolic execution we can explore other execution paths of the program.
after that we get the correct execution path, also the incorrect path, then we differentiate them to localize the different path conditions as errors.

## Slide 16: Control-flow analysis using symbolic execution
Collect more traces with their path conditions to analyze:
Pruning: Selective symbolic execution
Selectively applying symbolic execution on these branches:
route selection
export/import for target routes
peer connection establishment
…
…
Program
…
…
Program
Notes: to avoid exploring huge searching space, we use SSE to prune some paths.
It means We only apply SE to the route selection, export/import and peer connection branches.

## Slide 17: Control-flow analysis using symbolic execution
Collect more traces with their path conditions to analyze:
Data plane simulation
S
B
A
D
([D], Export(StaticBGP, T1))
([B, D], Export(StaticBGP, T1))
([S, A, D],
Export(StaticBGP, T1)) Import(SA, (T1, A, [D]))
([A, D], Export(StaticBGP, T1))
…
D(Static)
->D(BGP)
D->A
A->S
D->B
Export(StaticBGP, T1)?
Import (SA, (T1, A, [D]))?
F
T
T
F
Program
…
Conditions are attached as symbols with route announcements during the data plane simulation
Errors are configurations that deviate from those path conditions !
Notes: when D executes to the export branch, it supposes to go to the false branch, which means not to redistribute the static route to its BGP process, but the true branch is what we want to explore, so we make the export value as true and attach it as a symbol to the route
then keep executing using the symbolic route.
later we executes to the Import branch at S and we find that it will go to the false branch too, so we

## Slide 18: Diagnosis results
S
A
D
Property: S-*-D
Reality: There is no path from S to D
Error path conditions :
Export(StaticBGP, T1)) Import(SA, (T1, A, [D]))
Error1: The route-map in S (line 19, 22-24) filtered routes from A
Error2: There was no redistribution command in node D
Notes: we report all errors and related configuration lines of them, which is helpful for operators to fix the error.

## Slide 19: Evaluation
Evaluate Scalpel on synthetic configurations
Routing protocols: BGP, static route
Protocol features: redistribution, route filters
Networks size: O(10)~O(100) routers
O(100) lines of configuration per router
Errors injection: wrong-local-pref error, propagation-deny error, origin-deny error

## Slide 20: Evaluation: observable error diagnosis
For observable errors, all error traces can be generated < 4s
For observable errors, we diagnose all errors within several minutes
CRG generation time (s)
MUC and EI computation time (s)

## Slide 21: Evaluation : unobservable error diagnosis
Table: Diagnosis results on unobservable errors
Diagnosis time on unobservable errors (ms)
For unobservable errors, we diagnose 74% of them within 50ms

## Slide 22: Summary
We take the first step to apply program analysis to distributed router configuration diagnosis.
We design Scalpel, an automated router configuration diagnosis tool.
We implement Scalpel and demonstrate the capability of Scalpel.
Notes: questions 可以直接列

## Slide 23: Open questions
Non-deterministic execution (e.g., leveraging Hoyan’s design)
Supporting more protocols (e.g., link state protocols)
Scaling control-flow analysis for large networks (e.g., slicing)
Automatic repair based on diagnosis (e.g., constraint-based repair)
SNGroup site: http://sngroup.tech/
Contact us: sngroup.xmu@outlook.com
WeChat QR code
Notes: questions 可以直接列