## Slide 1: Network Layer: Distance Vector Protocols Variations Link-State Protocol
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf22/index.shtml
11/22/2022
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)

## Slide 3: Admin
Guest lectures are important 
Upcoming guest lectures
  December 1, Dr. Linghe Kong@SJTU,
  Internet of Things
  December 8, Dr. Zaoxing (Alan) Liu@Boston Univ.,
  Programmable Networks
  December 15, Dr. Zhenhua Li@THU,
  5G Network
Schedule is tentative

## Slide 4
Recap: Routing Context
Often depends on a graph abstraction:
graph nodes are routers
graph edges are physical links
  links have properties: delay, capacity, $ cost, policy
Goal: determine “good” paths
(sequences of routers) thru
networks from source to dest.
Routing
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 5: Recap: Routing Design Space
Routing has a large design space
  who decides routing?
    source routing: end hosts make decision
    network routing: networks make decision
  how many paths from source s to destination d?
    multi-path routing
    single path routing
  what does routing compute?
    network cost minimization (shortest path routing)
    QoS aware
  will routing adapt to network traffic demand?
    adaptive routing
    static routing
  …
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 6: Recap: Distance Vector Routing: Basic Idea (Bellman-Ford Alg)
At node i, the basic update rule
where
- di denotes the distance estimation from i to the destination,
- N(i) is set of neighbors of node i, and
- dij is the distance of the direct link from i to j
i
j
destination

## Slide 7: Understanding BFA and an Exercise of Primal-Dual
D
https://en.wikipedia.org/wiki/Shortest_path_problem#Linear_programming_formulation
=
xij is a flow from s to D

## Slide 8: Recap: Synchronous Bellman-Ford (SBF)
Nodes update in rounds:
  there is a global clock;
  at the beginning of each round, each node sends its estimate to all of its neighbors;
  at the end of the round, updates its estimation
A
B
E
C
D

## Slide 9: Recap: SBF/
Initialization (time 0):
A
E
D
C
B
7
8
10
2
1
2

## Slide 10: Example
A
E
D
C
B
7
8
10
2
1
2
A B C E D
d(0)
0
Consider D as destination; d(t) is a vector consisting of estimation of each node at round t
d(1)
2 2 0
d(2)
12 3 2 2 0
d(3)
10 3 2 2 0
d(4)
10 3 2 2 0
Observation: d(0) d(1) d(2) d(3) d(4) =d*

## Slide 11: A Nice Property of SBF: Monotonicity
Consider two configurations d(t) and d’(t)
If d(t) d’(t)
  i.e., each node has a higher estimate in one scenario (d) than in another scenario (d’),
then d(t+1) d’(t+1)
  i.e., each node has a higher estimate in d than in d’ after one round of synchronous update.

## Slide 12: Correctness of SBF/
Claim: di(h) is the length Li(h) of a shortest path from i to the destination using ≤ h hops
  base case: h = 0 is trivially true
  assume true for ≤ h, i.e., Li(h)= di(h), Li(h-1)= di(h-1), …

## Slide 13: Correctness of SBF/
consider ≤ h+1 hops:
since di(h) ≤ di(h-1)

## Slide 14
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distributed distance vector protocols
        synchronous Bellman-Ford (SBF)
          SBF/
          SBF/-1 SBF/

## Slide 15: SBF at another Initial Configuration: SBF/-1
Initialization (time 0):
A
E
D
C
B
7
8
10
2
1
2

## Slide 16: Example
A
E
D
C
B
7
8
10
2
1
2
A B C E D
d(0)
-1 -1 -1 -1 0
Consider D as destination
d(1)
6 0 0 2 0
d(2)
7 1 1 2 0
d(3)
8 2 2 2 0
d(4)
9 3 3 2 0
d(5)
10 3 3 2 0
Observation: d(0) d(1) d(2) d(3) d(4) d(5) = d(6) = d*
d(6)
10 3 3 2 0

## Slide 17: Correctness of SBF/-1
SBF/-1 converges due to monotonicity
Remaining question:
  Can we guarantee that SBF/-1 converges to shortest path?

## Slide 18: Correctness of SBF/-1
Common between SBF/and SBF/-1: they solve the Bellman equation
where dD = 0.
We have proven SBF/is the shortest path solution.
SBF/-1 computes shortest path if Bellman equation has a unique solution.

## Slide 19: Uniqueness of Solution to BE
Assume another solution d, we will show that d = d*
case 1: we show d d*
Since d is a solution to BE, we can construct paths as follows: for each i, pick a j which satisfies the equation; since d* is shortest, d d*
A
E
D
C
B
7
8
10
2
1
2
2
2
3
10

## Slide 20: Uniqueness of Solution to BE
Case 2: we show d ≤ d*
assume we run SBF with two initial configurations:
  one is d
  another is SBF/ (d∞),
  -> monotonicity and convergence of SBF/∞ imply that d ≤ d*

## Slide 21: Discussion
Will SBF converge under other non-negative initial conditions?
Problems of running synchronous BF?

## Slide 22
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distributed distance vector protocols
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)

## Slide 23: Asynchronous Bellman-Ford (ABF)
No notion of global iterations
  each node updates at its own pace
Asynchronously each node i computes
  using last received value dij from neighbor j.
Asynchronously node j sends its estimate to its neighbor i:
  We assume that there is an upper bound on the delay of estimate packet
Notes: Ti infinite
T^i_j infinite

## Slide 24: ABF: Example
A
E
D
C
B
7
8
10
2
1
2
d ()
A
B
C
D
E
distance tables from neighbors
destinations
computation
E’s
distance table
distance table E sends to its neighbors
A: 10
B: 8
C: 4
D: 2
E: 0
Below is just one step! The protocol repeats forever!
10 15
A B D
0 7
A B D
10 8 2
7 0
1 2
0
A: 10
B: 8
D: 4
D: 2
17 8
9 4
2

## Slide 25: Asynchronous Bellman-Ford (ABF)
ABF will eventually converge to the shortest path
  links can go down and come up – but if topology is stabilized after some time t and connected, ABF will eventually converge to the shortest path !

## Slide 26: ABF Convergence Proof Complexity: Complex System State
i
j
What is system state?
Notes: There are three types of distance estimates from node i:
d_i: current distance estimate at node i
- d^j_i: last d_i that neighbor j received
- d^j_i: d_i that are in transit to neighbor j

## Slide 27: System State
di
dj
dij
dij
three types of distance state from node j:
dj: current distance estimate state at node j
- dij: last dj that neighbor i received
- dij: those dj that are still in transit to neighbor i

## Slide 28: ABF Convergence Proof: The Sandwich Technique
Basic idea:
  bound system state using extreme states
Extreme states:
  SBF/; call the sequence U()
  SBF/-1; call the sequence L()
Notes: The state includes di, di_j, and messages containing di_j

## Slide 29: ABF Convergence
Consider the time when the topology is stabilized as time 0
U(0) and L(0) provide upper and lower bounds at time 0 on all corresponding elements of states
  Lj (0) ≤ dj ≤ Uj (0) for all dj state at node j
  Lj (0) ≤ dij ≤ Uj (0)
  Lj (0) ≤ update messages dij ≤ Uj (0)
Notes: The state includes di, di_j, and messages containing di_j

## Slide 30: ABF Convergence
dj
  after at least one update at node j: dj falls between Lj (1) ≤ dj ≤ Uj (1)
dij :
  eventually all dij that are only bounded by Lj (0) and Uj (0) are replaced with in Lj(1) and Uj(1)
di
dj
dij
dij
Notes: The state includes di, di_j, and messages containing di_j

## Slide 31: Asynchronous Bellman-Ford: Summary
Distributed
  each node communicates its routing table to its directly-attached neighbors
Iterative
  continues periodically or when link changes, e.g. detects a link failure
Asynchronous
  nodes need not exchange info/iterate in lock step!
Convergence
  in finite steps, independent of initial condition if network is connected

## Slide 32: Summary: Distributed Distance-Vector
Tool box: a key technique for proving convergence (liveness) of distributed protocols: monotonicity and bounding-box (sandwich) design
  Consider two configurations d(t) and d’(t):
    if d(t) <= d’(t), then d(t+1) <= d’(t+1)
  Identify two extreme configurations to sandwich any real configurations

## Slide 33
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV

## Slide 34: Properties of Distance-Vector Algorithms
Good news propagate fast

## Slide 35: Properties of Distance-Vector Algorithms
Bad news propagate slowly
This is called the counting-to-infinity problem
Q: what causes counting-to-infinity?
A-B link down

## Slide 36: Counting-To-Infinity is Because of Routing Loop
Counting-to-infinity is caused by a routing loop, which is a global state (consisting of the nodes’ local states) at a global moment (observed by an oracle) such that there exist nodes A, B, C, … E such that A (locally) thinks B as next hop, B thinks C as next hop, … E thinks A as next hop

## Slide 37
Discussion
Why avoid routing loops is hard?
Any proposals to avoid routing loops?

## Slide 38
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison

## Slide 39
The Reverse-Poison (Split-horizon) Hack
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
0
7
1
c(E,A)
B
7
0
1
8
c(E,B)
D
2
0
2
c(E,D)
E
distance tables from neighbors
destinations
A
1
8
B
15
8
9
D
4
2
computation
E’s
distance table
1, A
8, B
4, D
2, D
distance table E sends to its neighbors
distance
through
neighbor
To A
A:
B: 8
C: 4
D: 2
E: 0
To B
A: 1
B:
C: 4
D: 2
E: 0
To D
A: 1
B: 8
C:
D:
E: 0
If the path to dest is through neighbor h, report ∞ to neighbor h for dest.
39

## Slide 40: DV+RP => RIP ( Routing Information Protocol)
Included in BSD-UNIX Distribution in 1982
Link cost: 1
Distance metric: # of hops
Distance vectors
  exchanged every 30 sec via Response Message (also called advertisement) using UDP
  each advertisement: route to up to 25 destination nets
40

## Slide 41: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly propagates to entire net
  reverse-poison used to prevent ping-pong loops
  set infinite distance = 16 hops (why?)
41

## Slide 42: General Routing Loops and Reverse-poison
Exercise: Can Reverse-poison guarantee no loop for this network?

## Slide 43: General Routing Loops and Reverse-poison
Reverse-poison removes two-node loops but may not remove more-node loops
I can reach D w/ cost 3
Unfortunate timing can lead to a loop
  When the link between C and D fails, C will set its distance to D as
  A receives the bad news () from C, A will use B to go to D
  A sends the news to C
  C sends the news to B

## Slide 44
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison
            destination-sequenced DV (DSDV)

## Slide 45: Destination-Sequenced Distance Vector protocol (DSDV)
Basic idea: use sequence numbers to partition computation
  tags each route with a sequence number
  each destination node D periodically advertises monotonically increasing even-numbered sequence numbers
  when a node realizes that the link it uses to reach destination D is broken, it advertises an infinite metric and a sequence number which is one greater than the previous route (i.e., an odd seq. number)
    the route is repaired by a later even-number advertisement from the destination

## Slide 46: DSDV: More Detail
Let’s assume the destination node is D
There are optimizations but we present a simple version:
  each node B maintains (SB, dB), where SB is the sequence number at B for destination D and dB is the best distance using a neighbor from B to D
Both periodical and triggered updates
  periodically: D increases its seq. by 2 and broadcasts with (SD, 0)
  if B is using C as next hop to D and B discovers that C is no longer reachable
    B increases its sequence number SB by 1, sets dB to , and sends (SB, dB) to all neighbors
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.

## Slide 47: Example
1
1
5
1
X
Will this trigger an update?

## Slide 48: Example
1
1
5
1
X
Will this trigger an update?

## Slide 49: DSDV: Update Alg.
Consider simple version, no optimization
Update after receiving a message
  assume B sends to A its current state (SB, dB)
  when A receives (SB, dB)
      if SB > SA, then // always update if a higher seq#
        SA = SB
        if (dB == ) dA = ; else dA= dB + d(A,B)
      else if SA == SB, then
        if dA > dB + d(A,B) // update for the same seq# only if better route dA= dB + d(A,B) and uses B as next hop
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.