## Slide 1: Network Layer: Distance Vector Protocols Variations Link-State Protocol
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf22/index.shtml
11/22/2022
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)

## Slide 3: Admin
Guest lectures are important 
Upcoming guest lectures
  December 1, Dr. Linghe Kong@SJTU,
  Internet of Things
  December 8, Dr. Zaoxing (Alan) Liu@Boston Univ.,
  Programmable Networks
  December 15, Dr. Zhenhua Li@THU,
  5G Network
Schedule is tentative

## Slide 4
Recap: Routing Context
Often depends on a graph abstraction:
graph nodes are routers
graph edges are physical links
  links have properties: delay, capacity, $ cost, policy
Goal: determine “good” paths
(sequences of routers) thru
networks from source to dest.
Routing
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 5: Recap: Routing Design Space
Routing has a large design space
  who decides routing?
    source routing: end hosts make decision
    network routing: networks make decision
  how many paths from source s to destination d?
    multi-path routing
    single path routing
  what does routing compute?
    network cost minimization (shortest path routing)
    QoS aware
  will routing adapt to network traffic demand?
    adaptive routing
    static routing
  …
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 6: Recap: Distance Vector Routing: Basic Idea (Bellman-Ford Alg)
At node i, the basic update rule
where
- di denotes the distance estimation from i to the destination,
- N(i) is set of neighbors of node i, and
- dij is the distance of the direct link from i to j
i
j
destination

## Slide 7: Understanding BFA and an Exercise of Primal-Dual
D
https://en.wikipedia.org/wiki/Shortest_path_problem#Linear_programming_formulation
=
xij is a flow from s to D

## Slide 8: Recap: Synchronous Bellman-Ford (SBF)
Nodes update in rounds:
  there is a global clock;
  at the beginning of each round, each node sends its estimate to all of its neighbors;
  at the end of the round, updates its estimation
A
B
E
C
D

## Slide 9: Recap: SBF/
Initialization (time 0):
A
E
D
C
B
7
8
10
2
1
2

## Slide 10: Example
A
E
D
C
B
7
8
10
2
1
2
A B C E D
d(0)
0
Consider D as destination; d(t) is a vector consisting of estimation of each node at round t
d(1)
2 2 0
d(2)
12 3 2 2 0
d(3)
10 3 2 2 0
d(4)
10 3 2 2 0
Observation: d(0) d(1) d(2) d(3) d(4) =d*

## Slide 11: A Nice Property of SBF: Monotonicity
Consider two configurations d(t) and d’(t)
If d(t) d’(t)
  i.e., each node has a higher estimate in one scenario (d) than in another scenario (d’),
then d(t+1) d’(t+1)
  i.e., each node has a higher estimate in d than in d’ after one round of synchronous update.

## Slide 12: Correctness of SBF/
Claim: di(h) is the length Li(h) of a shortest path from i to the destination using ≤ h hops
  base case: h = 0 is trivially true
  assume true for ≤ h, i.e., Li(h)= di(h), Li(h-1)= di(h-1), …

## Slide 13: Correctness of SBF/
consider ≤ h+1 hops:
since di(h) ≤ di(h-1)

## Slide 14
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distributed distance vector protocols
        synchronous Bellman-Ford (SBF)
          SBF/
          SBF/-1 SBF/

## Slide 15: SBF at another Initial Configuration: SBF/-1
Initialization (time 0):
A
E
D
C
B
7
8
10
2
1
2

## Slide 16: Example
A
E
D
C
B
7
8
10
2
1
2
A B C E D
d(0)
-1 -1 -1 -1 0
Consider D as destination
d(1)
6 0 0 2 0
d(2)
7 1 1 2 0
d(3)
8 2 2 2 0
d(4)
9 3 3 2 0
d(5)
10 3 3 2 0
Observation: d(0) d(1) d(2) d(3) d(4) d(5) = d(6) = d*
d(6)
10 3 3 2 0

## Slide 17: Correctness of SBF/-1
SBF/-1 converges due to monotonicity
Remaining question:
  Can we guarantee that SBF/-1 converges to shortest path?

## Slide 18: Correctness of SBF/-1
Common between SBF/and SBF/-1: they solve the Bellman equation
where dD = 0.
We have proven SBF/is the shortest path solution.
SBF/-1 computes shortest path if Bellman equation has a unique solution.

## Slide 19: Uniqueness of Solution to BE
Assume another solution d, we will show that d = d*
case 1: we show d d*
Since d is a solution to BE, we can construct paths as follows: for each i, pick a j which satisfies the equation; since d* is shortest, d d*
A
E
D
C
B
7
8
10
2
1
2
2
2
3
10

## Slide 20: Uniqueness of Solution to BE
Case 2: we show d ≤ d*
assume we run SBF with two initial configurations:
  one is d
  another is SBF/ (d∞),
  -> monotonicity and convergence of SBF/∞ imply that d ≤ d*

## Slide 21: Discussion
Will SBF converge under other non-negative initial conditions?
Problems of running synchronous BF?

## Slide 22
Outline
Admin and recap
Network overview
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distributed distance vector protocols
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)

## Slide 23: Asynchronous Bellman-Ford (ABF)
No notion of global iterations
  each node updates at its own pace
Asynchronously each node i computes
  using last received value dij from neighbor j.
Asynchronously node j sends its estimate to its neighbor i:
  We assume that there is an upper bound on the delay of estimate packet
Notes: Ti infinite
T^i_j infinite

## Slide 24: ABF: Example
A
E
D
C
B
7
8
10
2
1
2
d ()
A
B
C
D
E
distance tables from neighbors
destinations
computation
E’s
distance table
distance table E sends to its neighbors
A: 10
B: 8
C: 4
D: 2
E: 0
Below is just one step! The protocol repeats forever!
10 15
A B D
0 7
A B D
10 8 2
7 0
1 2
0
A: 10
B: 8
D: 4
D: 2
17 8
9 4
2

## Slide 25: Asynchronous Bellman-Ford (ABF)
ABF will eventually converge to the shortest path
  links can go down and come up – but if topology is stabilized after some time t and connected, ABF will eventually converge to the shortest path !

## Slide 26: ABF Convergence Proof Complexity: Complex System State
i
j
What is system state?
Notes: There are three types of distance estimates from node i:
d_i: current distance estimate at node i
- d^j_i: last d_i that neighbor j received
- d^j_i: d_i that are in transit to neighbor j

## Slide 27: System State
di
dj
dij
dij
three types of distance state from node j:
dj: current distance estimate state at node j
- dij: last dj that neighbor i received
- dij: those dj that are still in transit to neighbor i

## Slide 28: ABF Convergence Proof: The Sandwich Technique
Basic idea:
  bound system state using extreme states
Extreme states:
  SBF/; call the sequence U()
  SBF/-1; call the sequence L()
Notes: The state includes di, di_j, and messages containing di_j

## Slide 29: ABF Convergence
Consider the time when the topology is stabilized as time 0
U(0) and L(0) provide upper and lower bounds at time 0 on all corresponding elements of states
  Lj (0) ≤ dj ≤ Uj (0) for all dj state at node j
  Lj (0) ≤ dij ≤ Uj (0)
  Lj (0) ≤ update messages dij ≤ Uj (0)
Notes: The state includes di, di_j, and messages containing di_j

## Slide 30: ABF Convergence
dj
  after at least one update at node j: dj falls between Lj (1) ≤ dj ≤ Uj (1)
dij :
  eventually all dij that are only bounded by Lj (0) and Uj (0) are replaced with in Lj(1) and Uj(1)
di
dj
dij
dij
Notes: The state includes di, di_j, and messages containing di_j

## Slide 31: Asynchronous Bellman-Ford: Summary
Distributed
  each node communicates its routing table to its directly-attached neighbors
Iterative
  continues periodically or when link changes, e.g. detects a link failure
Asynchronous
  nodes need not exchange info/iterate in lock step!
Convergence
  in finite steps, independent of initial condition if network is connected

## Slide 32: Summary: Distributed Distance-Vector
Tool box: a key technique for proving convergence (liveness) of distributed protocols: monotonicity and bounding-box (sandwich) design
  Consider two configurations d(t) and d’(t):
    if d(t) <= d’(t), then d(t+1) <= d’(t+1)
  Identify two extreme configurations to sandwich any real configurations

## Slide 33
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV

## Slide 34: Properties of Distance-Vector Algorithms
Good news propagate fast

## Slide 35: Properties of Distance-Vector Algorithms
Bad news propagate slowly
This is called the counting-to-infinity problem
Q: what causes counting-to-infinity?
A-B link down

## Slide 36: Counting-To-Infinity is Because of Routing Loop
Counting-to-infinity is caused by a routing loop, which is a global state (consisting of the nodes’ local states) at a global moment (observed by an oracle) such that there exist nodes A, B, C, … E such that A (locally) thinks B as next hop, B thinks C as next hop, … E thinks A as next hop

## Slide 37
Discussion
Why avoid routing loops is hard?
Any proposals to avoid routing loops?

## Slide 38
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison

## Slide 39
The Reverse-Poison (Split-horizon) Hack
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
0
7
1
c(E,A)
B
7
0
1
8
c(E,B)
D
2
0
2
c(E,D)
E
distance tables from neighbors
destinations
A
1
8
B
15
8
9
D
4
2
computation
E’s
distance table
1, A
8, B
4, D
2, D
distance table E sends to its neighbors
distance
through
neighbor
To A
A:
B: 8
C: 4
D: 2
E: 0
To B
A: 1
B:
C: 4
D: 2
E: 0
To D
A: 1
B: 8
C:
D:
E: 0
If the path to dest is through neighbor h, report ∞ to neighbor h for dest.
39

## Slide 40: DV+RP => RIP ( Routing Information Protocol)
Included in BSD-UNIX Distribution in 1982
Link cost: 1
Distance metric: # of hops
Distance vectors
  exchanged every 30 sec via Response Message (also called advertisement) using UDP
  each advertisement: route to up to 25 destination nets
40

## Slide 41: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly propagates to entire net
  reverse-poison used to prevent ping-pong loops
  set infinite distance = 16 hops (why?)
41

## Slide 42: General Routing Loops and Reverse-poison
Exercise: Can Reverse-poison guarantee no loop for this network?

## Slide 43: General Routing Loops and Reverse-poison
Reverse-poison removes two-node loops but may not remove more-node loops
I can reach D w/ cost 3
Unfortunate timing can lead to a loop
  When the link between C and D fails, C will set its distance to D as
  A receives the bad news () from C, A will use B to go to D
  A sends the news to C
  C sends the news to B

## Slide 44
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison
            destination-sequenced DV (DSDV)

## Slide 45: Destination-Sequenced Distance Vector protocol (DSDV)
Basic idea: use sequence numbers to partition computation
  tags each route with a sequence number
  each destination node D periodically advertises monotonically increasing even-numbered sequence numbers
  when a node realizes that the link it uses to reach destination D is broken, it advertises an infinite metric and a sequence number which is one greater than the previous route (i.e., an odd seq. number)
    the route is repaired by a later even-number advertisement from the destination

## Slide 46: DSDV: More Detail
Let’s assume the destination node is D
There are optimizations but we present a simple version:
  each node B maintains (SB, dB), where SB is the sequence number at B for destination D and dB is the best distance using a neighbor from B to D
Both periodical and triggered updates
  periodically: D increases its seq. by 2 and broadcasts with (SD, 0)
  if B is using C as next hop to D and B discovers that C is no longer reachable
    B increases its sequence number SB by 1, sets dB to , and sends (SB, dB) to all neighbors
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.

## Slide 47: Example
1
1
5
1
X
Will this trigger an update?

## Slide 48: Example
1
1
5
1
X
Will this trigger an update?

## Slide 49: DSDV: Update Alg.
Consider simple version, no optimization
Update after receiving a message
  assume B sends to A its current state (SB, dB)
  when A receives (SB, dB)
      if SB > SA, then // always update if a higher seq#
        SA = SB
        if (dB == ) dA = ; else dA= dB + d(A,B)
      else if SA == SB, then
        if dA > dB + d(A,B) // update for the same seq# only if better route dA= dB + d(A,B) and uses B as next hop
A
B
route update
Notes:       The step if SA > SB, then update may not be good because it maybe a cross talk.

## Slide 50: Example
1
1
5
1
Exercise: update process after D increases its seq# to next even number.

## Slide 51: Claim: DSDV will NEVER Form a Loop
Initially no loop (no one has next hop so no loop)
Derive contradiction if a loop forms after a node processes an update,
  e.g., when A receives the update from B, A decides to use B as next hop and forms a loop
A
B
update

## Slide 52: Technique: Global Invariants
Global Invariant is a very effective method in understanding safety of distributed asynchronous protocols
Invariants are defined over the states of the distributed nodes
Consider any node B.
Let’s identify some invariants over the state of node B, i.e., (SB, dB).

## Slide 53: Invariants of a Single Node B
Some invariants about the state of a node B
  [I1] SB is non-decreasing
  [I2] dB is non-increasing for the same sequence number
time

## Slide 54: Invariants of if A Considers B as Next Hop
Some invariants if A considers B as next hop
  [I3] dA is not
  [I4] SB >= SA
    because A is having the seq# which B last sent to A; B’s seq# might be increased after B sent its state
    [I5] if SB == SA
    then dB < dA because dA is based on dB which B sent to A some time ago, dB < dA since all link costs are positive; dB might be decreased after B sent its state
A
B

## Slide 55
Loop Freedom of DSDV
Consider a critical moment
  A starts to consider B as next hop, and we have a loop
According to invariant I4 for each link in the loop (X considers Y as next hop) : SY >= SX
Two cases:
  exists SY > SX
    by transition along the loop SB > SB
  all nodes along the loop have the same sequence number
    apply I5, by transition along the loop dB > dB
A
B
X
Y
update

## Slide 56: Issue of DSDV
1
1
5
1
X

## Slide 57
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
        synchronous Bellman-Ford (SBF)
        asynchronous Bellman-Ford (ABF)
        properties of DV
          DV w/ loop prevention
            reverse poison
            destination-sequenced DV (DSDV)
            diffusive update algorithm (DUAL) and EIGRP

## Slide 58: Basic Idea
DSDV guarantees no loop, but at the price of not using any backup path before destination re-announces reachability.
Basic idea: Sufficient condition to guarantee no loop using backup paths (called switching)?

## Slide 59: Key Idea: Feasible Successors
If the reported distance of a neighbor n is lower than the total distance using primary (current shortest), the neighbor n is a feasible successor
n
p
i

## Slide 60: Intuition
Since the reported distance of B is lower than my total distance, B cannot be using me (along a path) to reach the destination
A
feasible successor
primary
B
D
Notes: Before failure:
- dB < dA
- dB >= dC >= dD >= dE >= dA

## Slide 61: Example
Assume A is destination, consider E
 | Reported Dist. | Total Dist.
Neighbor C |  | 
Neighbor D |  | 
3
4
6
5

## Slide 62: Example
5
1
1
1

## Slide 63: Summary: Distance Vector Routing
Basic DV protocol
  take away: use monotonicity as a technique to understand liveness/convergence
    highly recommended reading of Bersekas/Gallager chapter
Fix counting-to-infinity problem
  DSDV
    Idea: uses sequence number to avoid routing loops
      seq# partitions routing updates from different outside events
      within same event, no loop so long each node only decreases its distance
    Analysis: use global invariants to understand/design safety/no routing loops
  EIRGP (DUAL)
    Idea: introduces a sufficient condition for local recovery
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 64: Discussion: Distance Vector Routing
What do you like about distributed, distance vector routing?
What do you not like about distributed, distance vector routing?
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 65: Churns of DV: One Example
N+2
…
…
1
2
3
N-1
N
N+1
N+3
2N
Initially converged.
All links have cost 1
Event: Cost of 1->2 reduces to 0
Message sequences
Node 2 tells 3. Node 3 tells 4…Node N tells N+1. (N-1 messages)
Node N+1 tells N+2, N+2 tells N+3,…,2N. (N-1 messages)
Now node N-1 tells node N+1
Step 2 repeats
Now node N-2 tells node N+1
…
A total of O(N2) messages

## Slide 66
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)

## Slide 67: Link-State Routing
Basic idea: Not distributed computing, only distributed state distribution
Net topology, link costs are distributed to all nodes
    all nodes have same info
    Each node computes its shortest paths from itself to all other nodes
      standard Dijkstra’s algorithm as path compute alg
      Allows multiple same-cost paths
      Multiple cost metrics per link (for type of service routing)
Most commonly used routing protocol (e.g., OSPF/ISIS) by most networks in Internet

## Slide 68: Example: Link State and Directed Graph (OSPFv2)
https://tools.ietf.org/html/rfc1583#page-12
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 69: Example: Link State and Directed Graph (OSPFv2)
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 70
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Distance vector protocols (distributed computing)
      Link state protocols (distributed state synchronization)
        data structure to be distributed
        state distribution protocol

## Slide 71: Basic Link State Broadcast Protocol
Basic event structure at node n
  on initialization:
    broadcast LSA[e] for each link e connected to n
  on state change to a link e connected to n:
    broadcast LSA[e] = new status
  on receiving an LSA[e]:
    if (does not have LSA[e]) forwards LSA[e] to all links except the incoming link
Notes: Need to setup order: Right after said a link is up, it became down
solution: sequence#
  ordering of events (link up and down)
  network partitioning and then merge
sequence# corruption: age
Partition: periodical rebroadcast
Failure

## Slide 72
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
Link State Broadcast
Node S updates link states connected to it.

## Slide 73
Link State Broadcast
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
To avoid forwarding the same link state announcement (LSA) multiple times (forming a loop), each node remembers the received LSAs.
- Second LSA[S] received by E from C is discarded
- Second LSA[S] received by C from E is discarded as well
- Node H receives LSA[S] from two neighbors, and will discard one of them

## Slide 74: Discussion
Issues of the basic link state protocol?
  Recall: goal is to efficiently distribute to each node to a correct, complete link state map

## Slide 75: Link State Broadcast: Issues
Problem: Out of order delivery
  link down and then up
  A node may receive up first and then down
Solution
  Each link update is given a sequence number: (initiator, seq#, link, status)
    the initiator should increase the seq# for each new update
  If the seq# of an update of a link is not higher than the highest seq# a router has seen, drop the update
  Otherwise, forward it to all links except the incoming link (real implementation using packet buffer)
  Problem of solution: seq# corruption
  Solution: age field (e.g., https://tools.ietf.org/html/rfc1583#page-102)

## Slide 76: Link State Broadcast: Issues
Problem: network partition and then reconnect, how to sync across the reconnected components
Solution: updates are sent periodically

## Slide 77: Link State Broadcast: Issues
Problem: Broadcast redundancy
https://hal.inria.fr/inria-00072756/document

## Slide 78: Hierarchical OSPF
“summarize” distances to nets in own area, advertise to other Area Border routers.
run OSPF routing limited to backbone.
  - Link-state advertisements only in area
  each nodes has detailed area topology; - only know direction (shortest path) to nets in other areas.
Two-level hierarchy: local area, backbone.

## Slide 79: Summary: Link State
Basic LS protocol
  take away: instead of computing routing results using distributed computing, distributed computing is for only link state distribution (synchronization)
Link state distribution can still have much complexity, e.g., out of order delivery, partition and reconnect, scalability
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.